PH 112 DC Circuit Worksheet  February 1, 2005  	(keep this one)

Ohm's law states that V = I R, where V is the potential difference across a resistor R with a current I flowing through the resistor.

Show that for two resistors in series the 				I

'equivalent' resistance is Req = R1 + R2.					+

The current I is the same for both. The

potential difference across the two V = V1 + V2.				     R1		V1

-

V

+

R2         V2

-

Show that for two resistors in parallel we          I				I

have an equivalent resistance Req such that

I

1/Req = 1/R1 + 1/R2

Req              V	R1	        R2

The parallel resistors have the same potential

difference V = V1 = V2, but the current

splits up between them:  I = I1 + I2.

Start with  V = I Req.

over for a circuit problem

-	+         2A

24v

R

-

I1		           I2

16 (

8 (

Use a loop equation to find the current I1.  (Lefthand loop)

Then find I2 by summing the currents at the top node.

Finally, find R. (Use a loop equation.)

a) I1 = 0.5 A       b) I2 = 1.5 A		c)    R = 5.33 ohms