PH 112 MJM   Rotational quantities worksheet	Name _____________________  Box #______

s

(

R		BASIC NOMENCLATURE

( = s/R		d(/dt = (		ds/dt = vT	R = constant, so	( = vT/R

( = vT/R	d(/dt = (		dvT/dt = aT	R = constant, so	( = aT/R

In linear motion with constant acceleration we had:		x = xo + vox t + 1/2 ax t2 .

Write down the analogous equation for rotation

with constant angular acceleration:

A wheel undergoes constant angular

acceleration from rest and completes

3.0 revolutions in 2.1 sec. Find its

angular acceleration of the disc, in rad/s2.

In linear motion with constant acceleration we had			vf2 = vi2 + 2 ax (xf-xi)

A wheel with angular velocity +2.3 rad/s decelerates

uniformly at -1.6 rad/s2 until its angular velocity is

-1.1 rad/s. How many revolutions did this require?

(just find the net angular displacement).

The convention is that positive angles are CCW

(counterclockwise) from the x-axis.

For an object rotating CW and slowing down	( is  ( pos.   neg  )          ( is  ( pos.   neg. )

(circle the correct ones)

For an object rotating CCW and speeding up		( is  ( pos.   neg  )          ( is  ( pos.   neg. )

(circle the correct ones)

(see back side for more)

Two masses are rigidly attached 					        m1

to a thin massless rigid sheet which rotates 				   v1	       r1

about an axis perpendicular to the page

through point p. The angular velocity	 (						p

is CCW around the pivot at p.

r2

m2

v2

Mass M is the linear inertia coefficient, the resistance to change of linear motion.

What we want to find is the rotational inertia coefficient, the resistance to change of rotational motion. This thing will eventually have the symbol I, meaning the 'moment of inertia', or the 'rotational inertia'.

We will try to get a formula like T = 1/2 Mv2 for

the kinetic energy of a rotating rigid body.

Start with T = 1/2 m1 v12 + 1/2 m2 v22  and

come up with a formula for T which contains

(. To do this you must realize that both

masses have the same ( .

You want to wind up with a formula which looks like

Tp = 1/2 Ip (2.

This is the rotational analog of  T = 1/2 Mv2,

and Ip is the 'rotational inertia'. It should contain

both masses and their distances from p.

Note that Ip depends on where the object is pivoted!

If the pivot p above were in the center of the circle,

I would be different.

ring			disc

Explain briefly why Iring,CM = MR2 while for a solid disc

the formula is Idisc,CM = 1/2 MR2 (M is the total mass,

and each is pivoted about the center of mass CM.)

Fill in the following table between linear and angular quantities

|  | displacement | velocity | inertia | KE | acceleration | momentum |
| --- | --- | --- | --- | --- | --- | --- |
| linear |  |  |  |  |  |  |
| angular |  |  |  |  |  |  |