RC Worksheet		MJM	February 4, 2005	Name_____________________ Box _____

C = q/V

(See text, p. 985)  We start with a charged capacitor						I

C having a charge q on it. The initial charge is Qo .		     + + + + +

We will close a switch at t=0 and begin to discharge        C                          q           +

the capacitor through the resistor.

- - - - - - -                            R

The charge q on the capacitor will be decreasing, so					 -

dq/dt will be negative. We want the current i in the

circuit to be positive, so we need

i = -dq/dt .

The loop equation during discharge is

q/C - iR = 0,   or    q/C - R dq/dt = 0.

We could multiply this by C and get

q + RC dq/dt = 0.

The second term must have units of charge, so RC must be a time!

And indeed 1 ohm-farad = 1second.    RC is called the 'time constant'.

Separating the equation gives  dq/q = -dt/(RC). this integrates to

Qo(q  dq/q = -0 (t dt/(RC)  =>  ln(q/Qo) = -t/(RC)  => q = Qo exp(-t/(RC))

Exercise:  Write the boxed equation in terms

of the capacitor voltage V.

Exercise: Calculate how much of the charge (or voltage)

is left after we have waited a time equal to 3 RC.

Exercise: Ditto except that we wait 6 time constants.

Exercise: Given a R = 2.5  ( and C = 21000 (F,

how long must we wait until this capacitor

has only 5% of its original charge left?

(more on the back)

We have a 6000 (F capacitor to be discharged through a 200 ohm resistor. How long do we

have to wait until the capacitor is 'practically discharged'  (Circle the 'best' choice) { We don't want to wait forever if we don't have to.}

a)  10-6 s	b)  10-3 s	c) 1 sec	d) 1000 sec	e) 106 sec

We have a 21000 (F capacitor charged to 3.0v.

This is to be discharged through a 470 ohm resistor.

How long will it take to discharge down to a voltage

of 0.75 v?

Calculate the time constant of the

following circuit, in seconds.

5(C				     6 k(

20 (C

4 k(		        12 k(