ES205  Analysis and Design of Engineering Systems:

Modeling-- We modeled systems using ideal elements and then applied basic principles to obtain governing differential equations.

Analysis-- We solved the governing equations to gain insight that can be used in designing systems.

-- Exact solutions

-- Numerical solutions (Simulink and Matlab)

-- Design Space

-- Other domains

-- s-domain

-- frequency domain

Design:

-- Worked in teams

-- Oral presentations

-- Peer evaluations

-- Report writing

Lecture Topics:

Modeling:

1) Mechanical Systems

2) Electrical Systems

3) Electromechanical Systems

4) Thermal Systems

5) Fluid Systems

6) Hydraulic Systems

7) Model Forms and Notation

Analysis:

1) Numerical Solutions

2) First Order Systems

3) Second Order Systems

4) Frequency Response Plots (Bode Diagrams)

1) Mechanical Systems

a) system elements such as mass, spring, and dampers

b) springs in series/parallel

c) gears

d) translational and rotational systems

Spring:                                                                 Damper:

Spring in Series:                                       Springs in Parallel:

Gears:

Translational System:                                                       Rotational System:

2) Electrical Systems

a) Resistance, Capacitance, Inductance

b) Complex Impedance

c) Complex Impedance in series and parallel

d) RLC circuits

e) Op Amps (two rules)

Resistor:                                            time domain                    s domain                   Impedance:

va - vb =  i R                   Va -Vb = I R                 ZR = R

Capacitor:

i  =  C             I  =            ZC =

Coil:

va - vb = L                  Va - Vb = Ls I                ZL = L s

Impedance in Series:                         Impedance in Parallel:

Zeq  =

Example RCL circuit:                                                 Op Amp Rules: if feedback

Rule 1:

Rule 2:

I1  - I2 - I3 = 0        (Eq 1)

Vi -Vo = I1 R        (Eq 2)                                           Common Op Amp Circuit:

I2  =    (Eq 3)

Vo - 0 = Ls I3         (Eq 4)

3) ElectricalMechanical systems

a) DC Motors--armature controlled

b) DC Motors-- field controlled

b) Combination systems

Armature Controlled DC Motor                       Field Controlled DC Motor:

Mathematical Models:

Armature Control Motor Model:                    Field Control Motor Model:

Electrical Model                                                  Electrical Model

(Eq 1)                                  (Eq 1)

and                          (Eq 2)                             (Eq 2)

and                           (Eq 3)

Mechanical Model                                                Mechanical Model

(Eq 3)                                         (Eq 4)

and                          (Eq 4)                     and                            (Eq 5)

vin = control voltage                                  vb = motor back emf

iA = armature current                                if = field current

T = motor torque                                    Td = disturbance torque on shaft

J = motor inertia                                       c = motor damping constant

ω= speed of motor

RA = Armature Resistance                         Rf = field resistance

LA = Armature inductance                         Lf = field inductance

KE =  motor back EMF  constant              KT = motor torque constant

4)  Thermal Systems

a) Conduction, Convection, Radiation

b) Lumped Capacitance

c) Biot Number

Conduction:                                                                  Lumped Thermal Storage System:

where k is the thermal conductivity

Convection:

where hc is the convection coefficient                                from Conservation of Energy:

Radiation:

or

where σ is the Stefan-Boltzman constant

and  ε is the emissivity

Test for Valid Lumped Thermal System:

If     Bi < 0.1 ,  then the system may be treated as a lumped thermal system.

where

Typical Lumped Thermal System Problem:

Model:

5) Fluid Systems

a)  Tank draining problems

Continuity Equation:                   Bernoulli's Equation with External Work Term:

= ρ v A

Conservation of mass:

or

Static fluid pressure:                    Discharge coefficient relationship:

=  Ae

Tank Draining:

6) Hydraulics:

Spool Valve:                                                   Piston:

= Kv  x

Lever:

7) Model forms and notation:                          Simulation Diagram:

a) Block and simulation diagrams

b) ODEs

c) Transfer functions

d) State space

e) Input-Output

DE Model (2nd order equation):

or

DE Model (Set of 1st order equation):

or

State Space Form:

Transfer Function:                                              Input/Output:

Analysis:

1) Numerical solutions (Simulink, Matlab, and Maple)

2)  First Order Systems                                            1st Order Standard Form:

a)  Standard form

b)  Free response

c)  Step response

d)  Harmonic response                                       where   τ  =  time constant

e)  System identification                                                 K =  static gain

and parameter estimation

Free Response:      f (t) = 0

Settling Time:

Step Response:    f (t) = A u(t)

Settling Time:

Static Gain:

Harmonic Response:   where  f (t) = A cos(ωf  t)   or    A sin(ωf  t)

Magnification factor:

Phase angle:

Steady State Response:

Measured from Plot

(lag)

3)  Second order systems

a) standard form

b) free response

c)  step response

d) harmonic excitation

e) system identification and parameter estimation

Free Response:     f(t) = 0:

Overdamped solution:

Underdamped solution:

Critically damped solution:

Logarithmic decrement:                                    Damped natural frequency

Damping ratio                                                    Undamped natural frequency

2% Settling Time:                                               1% Settling Time:

Second order systems...continued

Step Response:  f(t) = A u(t)

Overdamped:

and

Critically Damped:

Underdamped:

Logarithmic decrement:                                    Damped natural frequency

Damping ratio                                                    Undamped natural frequency

Steady State Response, xss or x∞   = K   (static gain)

Rise Time, Trise:

% Overshoot (%OS):

2% Settling Time:                                                 1% Settling Time:

Second order systems...continued

Harmonic response:            f(t) =  A cos(ωf t + λ)   or   A sin(ωf t +λ)

= undamped natural freq.

ζ = damping ratio

K = static gain

Steady-State response:

Magnification factor:                                                       Output Phase angle:

Normalized frequency                                                       Measured from Plot

Phasor Notation:

C =  a + i b =  C  eiθ    =  C  θ

where   C =

and    θ =  tan-1(b/a)

Mulitple Harmonic Input Response:

or

where                                                            and

4) Frequency response plots (Bode Plots)

a) Read magnitude and phase to find steady state response

c) Interpreting Bode plots to find transfer function

d) Straight line asymptotic approximations system identification

e) Exact frequency analysis with Matlab and/or Maple

Term Type:   TF:                     Log Magnitude                                  Phase Angle

--------------------------------------------------------------------------------------------------------------------.

Constant        K

Gain

-------------------------------------------------------------------------------------------------------------------.

Pole/zero        sn

at

origin

----------------------------------------------------------------------------------------------------------------.

1st order Pole

not at origin

1st order Zero

not at origin

-----------------------------------------------------------------------------------------------------------------.

2nd order Pole

2nd order Zero

# Text boxes

k1

k2

k3

k3

k2

k1

x1

x2

keq

v2(t)

v1(t)

c

N2

N1

θ2

s1  s2

θ1

R2

R1

kθ

J

c

k

m

x(t)

f(t)

cv

kx

f(t)

m

B

T

θ

a

α

J

Bω

T

kθθ

R

vB

vA

i

vB

i

C

vA

vA

L

vB

i

vo

Z1

i3

Z3

Z2

Z1

Z3

Z2

Zeq = Z1 + Z2 + Z3

i2

C

L

R

i1

vi(t)

Vi

Z1

Z2

+

-

Vo

Vp

-

In

+

Vn

Ip

RA

LA

+

θM, ωM

vb

KE,KT

iA

-

if

J, c

Td

vin

+

θM, ωM

vb

KE,KT

-

iA

J, c

Td

Lf

Rf

vin

if

.

Qin

.

Qout

Usys

.

Win

Tfluid

.

Q

Cth = m c

T

Rconv

.

Q

hc

Tfluid

T

m

.

hexit

Vi

Ve

h

y

System

.

V

y

Kv

.

V

.

V

x

L1

L2

z

x

1

KA

..

x

.

x

KC

KB

x

f

+

-

-

m

t-to =4τ

t-to= 3τ

t-to= 2τ

t-to = 1τ

Response

t-to=0τ

initial slope =

98%

95%

86%

63%

KA uo

t

0

t = 2τ

t = 3τ

t = τ

95%

of Xo

86%

of Xo

63%

of Xo

Xo

t

Aexit

Ao

Ai

t

t

t

t

t

t

Ao

Ai

0o

-180o

for  K<0

0o

for  K>0

0 db

20 log10(K)

20 db/dec log10(K)

0o

0 db

180o

n=2

n=1

n= -1

n= -2

90o

-90o

-180o

n= -2

n= -1

n=1

n=2

-20 db/dec log10(K)

-40 db/dec log10(K)

40 db/dec log10(K)

0o

-45 o/dec log10(K)

10*ωbreak

0.1*ωbreak

-90o

0 db

ωbreak

-20 db/dec log10(K)

0 db

ωbreak

+20 db/dec log10(K)

0o

+45 o/dec log10(K)

10*ωbreak

0.1*ωbreak

90o

0o

-90 o/dec log10(K)

10*ωbreak

0.1*ωbreak

-180o

0 db

ωbreak

+40 db/dec log10(K)

0 db

ωbreak

-40 db/dec log10(K)

+90 o/dec log10(K)

0o

10*ωbreak

0.1*ωbreak

180o

F

F

F

F

LA

RA

F(s)

X(s)

ω =1

Ai

.