Let us consider a circuit with two energy storage elements.  In this problem, we concentrate on finding the initial conditions of the circuit.

For the circuit shown below, the switch has been opened for a long time and it is closes at t=0. Determine the initial values of the inductor and capacitor voltages and currents. ,, ,.

An instantaneously change in inductor current is impossible because the infinite voltage would be required. This means the inductor current must be continuous.

.

Electric charge in a capacitor can not change instantaneously. So q(t) must be continuous over time. Recall that q(t)=Cv(t). Thus the voltage across a capacitor cannot change instantaneously.

Let’s take a look on the circuit immediately before the switching. The circuit is in steady state mode since the source is dc and the switch has been open for a long time. So the capacitor behaves as open circuit and the inductor behaves as a short circuit.

KVL loop 1: voltage drop +

KVL loop 1: voltage drop: