OE 450	Spring Term 2005

Laser Physics

Assignment #1

Due:  March 22, 2005

- Derive an expression for the coherence length (in vacuum) of an optical source that has a frequency bandwidth ((; express you answer in terms of the linewidth, ((0, and the mean wavelength, .

- A magnetic-field technique for stabilizing a He-Ne laser to 2 parts in 1010 has been patented.  At 632.8 nm, what is the coherence length of a laser with such frequency stability?

- Determine the first few modes of a closed rectangular cavity that is 5.0 mm ( 5.0 mm (     1.0 mm.  If you were asked to provide a single mode laser, what wavelength would it operate at and what would be the maximum bandwidth of the gain media in the laser you propose.

- (A) Prove that the spherical wave expression

satisfies the Helmholtz equation.

(B) Verify the condition

where

for the validity of

.

5.	(Saleh and Teich 3.1-1)  The light from a Nd:YAG laser at wavelength 1.06 (m is a Gaussian beam of 1-W optical power and full angle beam divergence of 1 mrad.  Determine the beam waist radius, the depth of focus, the maximum intensity and the intensity on the beam axis at a distance of 100 cm from the location of the beam waist.