OE 450	Spring Term 2005

Laser Physics

Assignment #5

Due:  May 19, 2005

- Explain why so much more power can be obtained from a Q-switched laser than in ordinary continuous-wave (CW) operation.  (B) Describe some methods for Q-switching a laser (do not just list them but describe, briefly, how they work).

- Explain the difference between a Q-switched laser and a mode locked laser.  Which laser offers the highest repetition rate and which one offers the highest peak pulse energy?  Explain your responses.

- Consider the 632.8 nm He-Ne laser with a gain bandwidth of 1700 MHz.  (A) Estimate the shortest pulse that can be obtained by mode-locking such a laser.  (B) What is the duration of each pulse of the mode-locked train if the cavity has a mirror separation of 40 cm?  (C) What is the separation between the mode-locked pulses of part (B)?  (D) Why do liquid dye and solid-state lasers produce much shorter mode-locked pulses than typical gas lasers?

- Explain why much less power is needed to get a four-level system to lase than a three-level system (all other factors being more or less the same).

- Define optical pumping and describe and example.

- Define nonradiative decay and describe an example.

- Consider the 694.3 nm cw ruby laser with a Lorentzian lineshape of width (HWHM)         170 GHz.  Assume that the system has a decay rate (21 ( 5.0 ( 102 sec-1, the density of the active atoms NT ( 1.6 ( 1019 cm-3 and that the energy difference between the lowest level and the pump level (level 3) is about 3.6 ( 10-12 erg.   (A) Determine the approximate pumping power density necessary for the system to just begin to lase.  Assuming further that the ruby rod is 5.0 cm long and has a radius of 2 mm,  (B) determine the required pump power.  The lifetime for spontaneous emission is roughly 4.34 ( 10-3 sec and the index of refraction for ruby is about 1.76.   (C) Calculate the stimulated emission cross section, (.