Physics I

Homework VIII                                                                                                                 CJ

Chapter 8: 15, 20, 30, 38, 40, 46

8.15.  Model: The two hanging blocks, which can be modeled as particles, form two systems. The other two systems are the two knots where rope 1 meets with rope 2 and rope 2 meets with rope 3. All the four systems are in static equilibrium. The ropes are assumed to be massless.

| Visualize: |  |
| --- | --- |

Solve: (a) We will consider both the two hanging blocks and the two knots. The blocks are in static equilibrium with  Note that there are three action/reaction pairs. For Block 1 and Block 2,  and we have

Then, by Newton’s third law:

The knots are also in equilibrium. Newton’s law applied to the left knot is

The y-equation gives  Substitute this into the x-equation to find

Newton’s law applied to the right knot is

These can be combined just like the equations for the left knot to give

But the forces  and  are an action/reaction pair, so . Therefore,

We can now use the y-equation for the right knot to find .

8.20. Model: Sled A, sled B, and the dog (D) are treated like particles in the model of kinetic friction.

| Visualize: |  |
| --- | --- |

Solve: The acceleration constraint is  Newton’s second law on sled A is

Using fA  (knA, the x-equation yields

On sled B:

and  act as if they are an action/reaction pair, so  Using  , we get

Thus the tension T2  270 N.

8.30. Model: Masses m1 and m2 are considered particles. The string is assumed to be massless.

| Visualize: |  |
| --- | --- |

Solve: The tension in the string causes the centripetal acceleration of the circular motion. If the hole is smooth, it acts like a pulley. Thus tension forces  and  act as if they were an action/reaction pair. Mass m1 is in circular motion of radius r, so Newton’s second law for m1 is

Mass m2 is at rest, so the y-equation of Newton’s second law is

Newton’s third law tells us that . Equating the two expressions for these quantities:

8.38. Model: Assume the particle model for the book (B) and the coffee cup (C), the models of kinetic and static friction, and the constant-acceleration kinematic equations.

| Visualize: |  |
| --- | --- |

Solve: (a) Using ,

To find x1, we must first find a. Newton’s second law for the book and the coffee cup is

The last two equations can be rewritten, using aC  aB  a, as

Adding the two equations,

Using this value for a, we can now find x1 as follows:

(b) The maximum static friction force is  We’ll see if the force fs needed to keep the book in place is larger or smaller than  When the cup is at rest, the string tension is  Newton’s first law for the book is

 8.25 N

Because  the book slides back down.

8.40. Model: Use the particle model for the two blocks. Assume a massless rope, and massless, frictionless pulleys.

| Visualize: |  |
| --- | --- |

Note that for every meter block 1 moves forward, one meter is provided to block 2. So each rope on m2 has to be lengthened by one-half meter. Thus the acceleration constraint is

Solve: Newton’s second law for block 1 is T  m1a1. Newton’s second law for block 2 is 2T – w2  m2a2. Combining these two equations gives

where we have used .

Assess: If m1  0 kg, then a2  –g. This is what is expected for a freely falling object.

8.46.  A 1.0 kg wood block is placed behind a 2.0 kg wood block on a horizontal table. The coefficients of kinetic friction with the table are 0.3 for the 1.0 kg block and 0.5 for the 2.0 kg block. The 1.0 kg block is pushed forward, against the 2.0 block, and released with a speed of 2.0 m/s. How far do the blocks travel before stopping?

| Visualize: |  |
| --- | --- |

Solve: The 2.0 kg block in front has a larger coefficient of friction. Thus the 1.0 kg block pushes against the rear of the 2.0 kg block and, in reaction, the 2.0 kg block pushes backward against the 1.0 kg block. There’s no vertical acceleration, so n1  m1g and n2  m2g, leading to f1  1m1g and f2  2m2g. Newton’s second law along the x-axis is

where we used a1  a2  a. Also, F1 on 2  F2 on 1 because they are an action/reaction pair. Adding these two equations gives

We can now use constant-acceleration kinematics to find