Physics II

Homework VIII                                                                                                                      CJ

Chapter 19; 10, 16, 22, 32, 46

19-10:	a)	The relevant expressions are

- (Take A, k and ( to be positive.  At t = 0, the wave is represented by

Fig. (19-6(a)); point (i) in the problem corresponds to the origin, and

points (ii)-(vii) correspond to the points in the figure labeled 1-7).

- vy = (A cos(0) = (A, and the particle is moving upward (in

the positive y-direction).  ay = -(2 sin(0) = 0, and the particle is instantaneously not accelerating.  (ii) vy = (A cos(-(/4) = (A/ and the particle is moving up.  ay = -(2A sin (-(/4) = (2 A/ and the particle is speeding up.  (iii) vy = ( Acos(-(/2) = 0, and the particle is instantaneously at rest.  ay = -(2 A sin(-(/2) = (2 A, and the particle is speeding up.  (iv) vy = (A cos(-3(/4) = -(A/ and the particle is moving down.  ay = -(2 A sin(-3(/4) = ( 2 A/, and the particle is slowing down (vy is becoming less negative).  (v)   vy =-( A cos(-() = -(A and the particle is moving down.  Ay = -(2 A sin(-() = 0, and the particle is instantaneously not accelerating.  (vi) vy = ( A cos(-5(/4) = -(A/and the particle is moving down.  ay = (2 A sin(-5(/4) = -(A/ and the particle is speeding up (vy and ay have the same sign).  (vii) vy = (A cos (-3(/2) = 0, and the particle is instantaneously at rest.  ay = -(2A sin(-3(/2) = -(2A and the particle is speeding up.  (vii) vy = (A cos (-7(/4) = (A/ and the particle is moving upward.  ay = -(2A sub(-7(/4) = -(2A/ and the particle is slowing down (vy  and ay have opposite signs).

19-16:	a)

- ( = v/f = (41.8 m/s)/(1.20 Hz) = 34.9 m.

- The speed is larger by a factor of  and so for the same wavelength, the frequency must be multiplied by  or 1.70 Hz.

  - a), b), c)  Using Eq. (19-27),

- Repeating the calculation of Example 19-7 at T = 300.15 K gives vair = 348 m/s, and so = 3.80 vair, vHe = 2.94 vair and vAr = 0.928 vair.

19-32:	a)	From comparison with Eq. (19-4), A = 0.75 cm, ( =  =

5.00 cm, f = 125 Hz, T =  = 0.00800 s and v = (f = 6.25 m/s.

b)

- To stay with a wavefront as t increases,  x decreases and so the wave is moving in the –x-direction.

- From Eq. (19-13), the tension is F = (v2 = (0.50 kg/m)(6.25 m/s)2 = 19.5 N.

- Pave =

19-46:	a)	The tension is the difference between the diver’s weight and the buoyant

force,

F = (m - (waterV)g = (120 kg – (1000 kg/m3)(0.0800 m3)(9.80 m/s2)) = 392 N.

- The increase in tension will be the weight of the cable between the diver and the point at x, minus the buoyant force.  This increase in tension is then

((x - ((Ax))g = (1.10 kg/m – (1000 kg/m3)((1.00 x 10-2 m)2) (9.80 m/s2x

= (7.70 N/m)x.

The tension as a function of x is then F(x) = (392 N) + (7.70 N/m)x.

- Denote the tension as F(x) = F0 + ax, where F0 = 392 N and

a = 7.70 N/m.  Then, the speed of transverse waves as a function of

x is v =  and the time t needed for a wave to reach the

surface is found from

Let the length of the cable be L, so