Physics II

Homework X                                                                                                                    CJ

Chapter 28; 4, 8, 11, 14, 35, 43, 51

28.4. Solve: Equation 28.2 is. Using Table 28.1 for the electron density, we get

28.8. Model: Use the conduction model to relate the drift speed to the electric field strength.

Solve: From Equation 28.7, the electric field is

28.11. Model: A battery is a charge escalator.

Solve: When a wire is connected to a battery, there is a sustained motion of electrons. A current of 1.5 A means that a charge of 1.5 C flows through a cross section of the wire per second. Because , the number of electrons transported per second is

electrons

| 28.14. Visualize: |  |
| --- | --- |

The direction of the current  in a material is opposite to the direction of motion of the negative charges and is the same as the direction  of motion of positive charges.

Solve: The charge due to positive ions moving to the right per second is

The charge due to negative ions moving to the left per second is

Thus, the current in the solution is

28.35. Model: The current is the rate at which the charge of the ions moves through the ionic solution.

Solve: Because the atomic mass of gold is 197 g, the number of gold atoms is

atoms

We need to deposit N  1.528 ( 1021 gold ions, each with a charge of (1.60 ( 10(19 C, in 3 hours on the statue. The current is

| 28.43. Visualize: |  |
| --- | --- |

Solve: (a) Consider a spherical surface inside the hollow sphere at a radial distance r from the center. The current is flowing outward through this surface, which has surface area  Thus

Thus the electric field strength at radius r is

(b) For copper, with (  6.0 ( 107 ((1m(1,

28.51. Model: Because current is conserved, the currents in the two segments of the wire are the same.

Visualize: Please refer to Figure P28.51.

Solve: The currents in the two segments of the wire are related by I1  I2  I. But I  AJ, so we have A1J1  A2J2. The wire’s diameter is constant, so J1  J2 and (1E1  (2E2. The ratio of the electric fields is