Physics II

Homework III                                                                                                                   CJ

Chapter 14; 6, 16, 20, 23, 34, 44, 51, 76

14.6. Model: The oscillation is the result of simple harmonic motion.

Visualize: Please refer to Figure Ex14.6.

Solve: (a) The amplitude A  20 cm.

(b) The period T  4.0 s, thus

(c) The position of an object undergoing simple harmonic motion is . At  Thus,

Because the object is moving to the right at t  0 s, it is in the lower half of the circular motion diagram and thus must have a phase constant between ( and 2( radians. Therefore, .

14.16. Model: The mass attached to the spring is in simple harmonic motion.

Solve: (a) The period is

(b) The angular frequency is

(c) To calculate the phase constant ,

Because the mass is moving to the right at t  0 s, it is in the lower half of the circular motion diagram. Hence,

(d) At t  0 s,  becomes

(e) The maximum speed .

(g) At t  1.3 s, .

(h) At t  1.3 s, .

14.20. Model: The vertical oscillations constitute simple harmonic motion.

Solve: To find the oscillation frequency using , we first need to find the spring constant k. In equilibrium, the weight mg of the block and the spring force k(L are equal and opposite. That is, . The frequency of oscillation f is thus given as

14.23. Model: Assume the small-angle approximation so there is simple harmonic motion.

Solve: The period is  and is given by the formula

14.34. Visualize: Please refer to Figure P14.34.

Solve: The position and the velocity of a particle in simple harmonic motion are

From the graph, T  12 s and the angular frequency is

(a) Because , we have

(b) At t  0 s,

Because the velocity at t  0 s is negative and the particle is slowing down, the particle is in the second quadrant of the circular motion diagram. Thus

(c) At t  0 s, .

14.44. Solve: (a) The velocity is –0.25 m/s at times that satisfy the equation

The time is

This is a time at which v  –0.25 m/s, but it’s not a time after t  0 s. But the sine function is periodic with period 2 rad, so another angle whose sine is 0.7143 is

This is a time t > 0 s at which v  –0.25 m/s.

(b) The amplitude is A  vmax/  (0.35 m/s)(20 rad/s)  0.0175 m  1.75 cm. Thus the position at t  0.197 s is

14.51. Model: The compact car is in simple harmonic motion.

Solve: (a) The mass on each spring is . The spring constant can be calculated as follows:

(b) The car carrying four persons means that each spring has, on the average, an additional mass of 70 kg. That is, . Thus,

Assess: A small frequency change from the additional mass is reasonable because frequency is inversely proportional to the square root of the mass.

14.76. Model: The two springs obey Hooke’s law. Assume massless springs.

Visualize: Each spring is shown separately. Note that (x  (x1  (x2.

Solve: Only spring 2 touches the mass, so the net force on the mass is Fm  F2 on m. Newton’s third law tells us that F2 on m  Fm on 2 and that F2 on 1  F1 on 2. From Fnet  ma, the net force on a massless spring is zero. Thus Fw on 1  F2 on 1  k1(x1 and Fm on 2  F1 on 2  k2(x2. Combining these pieces of information,

Fm  k1(x1  k2(x2

The net displacement of the mass is (x  (x1  (x2, so

Turning this around, the net force on the mass is

keff, the proportionality constant between the force on the mass and the mass’s displacement, is the effective spring constant. Thus the mass’s angular frequency of oscillation is

Using  and  for the angular frequencies of either spring acting alone on m, we have

Since the actual frequency f is simply a multiple of , this same relationship holds for f: