TEST I: PH113 PHYSICS III (Sample)

Name:______________________				Box No.:_______________

1. Answer all questions.

2. All questions carry equal points.

| Problem number | Score |
| --- | --- |
| Problem (1) 25 points |  |
| Problem (2) 25 points |  |
| Problem (3) 25 points |  |
| Problem (4) 25 points |  |
| Total -- 100 points |  |

- An electron traveling with a velocity v = (5.00i + 4.00j - 6.80k) x 104 m/s enters a region of space where there is a magnetic field B = (25.0i + 50.0j + 20.0k) T.

- Sketch the two vectors.

- Compute the direction and magnitude of the magnetic force experienced by the electron.

- Will this particle make any circular motion? If so what is its radius?

- Two wires 25.0 cm long , separated by d = 2.54 cm, each carry a current I = 5.00 A. Wire one carries current into the plane of the page and wire 2 carries current out of the page.

- Find the magnitude and direction of the magnetic field produced by these two wires at a distance of 5.00 cm from wire one.

- What is the force experienced by wire one due to wire two?

- A circular coil of wire consists of exactly 500 turns with a 5.00-cm radius and a magnetic field is directed through the loop, perpendicular to its plane. The magnetic field starts with a magnitude of 1.0 T and is increased in strength at a rate of 0.600 T/s. The total resistance of the coil is 10.0 (.

- Draw a picture and show the magnetic field and the induced current. Determine the initial flux through the coil.

- Determine the emf generated in the coil.

- What is the current in one loop of the wire?

- A 2000-turn solenoid shown in the figure is 50.0 cm in length and has a diameter of 8.00 cm. Around the solenoid is wrapped a 25-turn coil attached to a resistance R = 100. . If the current in the solenoid is reduced at a rate from 5.00 A to 1.00 A in 0.25 s, What is the magnitude and direction of the induced current through the resistance in the coil wrapped around the solenoid?

Relevant equations:

Constants:

e = 1.6 x 10-19 C

o= 4  x 10-7 T.m/A

me= 9.109 x 10-31 kg