PH 404 Final Exam Laundry List							2/13/04

(l-lo)/lo = (1/Y) F/A		(d-do)/do = -((/Y) F/A		(Y/() (2 (4y/(x4 = -(2y/(t2

impedance = force/velocity	c2 = (RT/M			R = 8.31 J/mol(K

(air = 1.21 kg/m3 ,  cair = 343 m/s at 20 oC,  		(water = 1000 kg/m3, 		cwater = 1500 m/s.

Lp  = 10 log10 (p/po)2  = 20 log10 (p/po)		Y/( (2 k4 = (2

c2 = (RT/M	                  d(EV)/dt = P - Aabs Ec/4,

Ls =  20 log10([Vout/p]/[1V/(bar])			<I> = |p|2/(2(c)

<I> = |A|2/(2(c r2)  					TL = 10 log (1/()

=========================================================================

Simple harmonic motion: be able to

identify the 'phase' of a wave

determine the maximum velocity, given the amplitude and frequency

know that for a mass-spring system  ( = ((k/m)

Waves on strings: be able to

write down the equation of a 'standing wave'

resonance on a string: displacement = 0 at fixed end; slope=0 at free end

write down the equation of a 'travelling wave', and know what the 'phase' of the wave is

know that c = ((T/(), where ( is the mass/length of the string

For a wave y(x,t) = A exp(ikx-i(t), given Z = Fy/vy, show that impedance Z = T/c

Stress and Strain

Y = young's modulus = E = stress/strain

be able to use Dr. Meeks equations (4.1) for strain and poisson's ratio

know the definition of stress, and the definition of strain

Waves on bars

longitudinal waves: c = ((E/()   (E = young's modulus)

Find the longitudinal wave speed in a bar, given its density and young's modulus.

free end of bar: slope is zero, fixed end of bar; displacement zero

longitudinal resonances are much like those of the string

Waves on bars

transverse waves:  (this will be given) 	Y/( (2 k4 = (2

know what ( represents, and that ( for a circular bar is a/2

be able to calculate ( for a rectangular bar of width w and height h, and show it is h/(12

for the free-free bar   kL/2 = ( 3.011, 5, 7, 9, 11, etc) (/4

be able to calculate the lowest couple of transverse frequencies of a free-free bar of radius a,

given Y, (, a and L, and the equation Y/( (2 k4 = (2

Waves in 3-D

know that in general in 3-D  c2 = B/( .

Find the bulk modulus of water, given its sound speed of 1500 m/s and its density of 1000 kg/m3.

be able to calculate the speed of sound in a gas, from c2 = (RT/M

standing waves in an air column:

acoustic pressure is zero at a free end, maximum at a closed end

acoustic velocity is max at a free end, zero at a closed end

for a pipe open at both ends, be able to calculate the lowest two resonant frequencies

ditto for a pipe open at one end and closed at the other

be able to write down the equation of standing waves for resonances in air columns

=====================================================================

Be able to calculate the specific acoustic impedance (p/v) of a closed side branch.

know that v = p/((c) for a plane wave travelling to the right (+x) and v=  -p/((c) if going to the left

partitions

know that velocity must be the same for incoming, outgoing waves and the partition

write down F = ma for the partition

Be able to show that pi/pt  = 1 + i((/2(c (( = mass/area) for a flat partition. (text sect 12.3 p 263)

given pi/pt, and (c for air, calculate the insertion loss in db for a given partition at a particular frequency

room reverberations

Given   d(EV)/dt = P - Aabs Ec/4,	 sects 11.4 - 11.7

calculate the steady-state energy density E in a room, given P and absorber data

calculate the time constant for decay of sound in a room, given absorber data

microphone sensitivity calc to give pressure, V, dB etc.  p. 170

sect 3-11 db  and adding noises/sounds

given several dB readings be able to calculate an average dB value

given a dB reading of A and B, and another of B, figure out the dB reading for A alone.

calc radiated power from point source

know that the pressure from a spherically outgoing wave is p = A/r exp(ikr-i(t)

given that radiated intensity is <I> = 1/2 |p|2/((c), and the pressure from a point source is

p = A exp(ikr-i(t)/r, that the total radiated power from a point source is 2( A2/(c

Make an argument for a point source radiating twice as much power next to an infinite rigid wall as it would in empty space.

Calculate the duct transmission coefficient for a simple area expansion, where the duct area changes from A1 to A2 at x=0.   Does this depend on frequency?

If we mount a 40-kHz ultrasonic 'point source' a vertical distance D above a flat surface, and we have a detector a horizontal distance H away from the source, calculate the vertical height h>0 of the first maximum and first minimum signal in the detector.

Calculate the Q of a damped oscillator given a curve of response vs. frequency  from f/(f2-f1)

Lp  = 10 log10 (p/po)2  = 20 log10 (p/po),

where po = 20 (Pa.  Lp is often called the ‘sound power level’ (SPL),

Show this can also be written

Lp  = 10 log10 (I/Io), where Io = 10-12 w/m2.

be able to use the Ls formula to calculate a microphone sensitivity given Ls in dB.

Ls =  20 log10([Vout/p]/[1V/(bar])

know how to convert (bar to Pa.

Be able to do probs like Raichel 9.1 and 9.2, given Lp and Ls

Be able to write down the formula for the resonant frequency of a helmholtz resonator, and explicitly verify it has the right units.  ( ( = c (A/(LV)) ).

Sketch the shape of the transmission curve for a helmholtz resonator as a duct sidebranch, given A, L, V of the resonator.

You are not responsible for 'end corrections' to open pipes.

Verify that Bair = 1.4 P for air from data given.   Find B for water from data given.