PH 112 capacitance lab analysis		MJM   					Feb 6. 2007

Charging data	C1			i and slope w/ uncertainty

C2			i and slope w/ uncertainty

C1 parallel C2		i and slope w/ uncertainty

C1 series C2		i and slope w/ uncertainty

Discharging data (RC)

C1			R and slope w/ uncertainty

C2			R and slope w/ uncertainty

Charging one or  more capacitors

with constant current		    Calculated from C1 and C2	  Discharge thru  R  (RC)      Agree w/i error?

A	C1 ( (  )							  G . C1 ( (  )			Y/N

B	C2 ( (  )							  H. C2 ( (  )			Y/N

C	(C1 parallel C2)  ( (  )	     E  (C1 parallel C2)  ( (  )					Y/N

D	(C1 series C2)  ( (  )	     F (C1 series C2)  {no error calc}					Y/N

Do A and G agree within error?

Do B & H agree within error?

Do C and E agree within error?

Do D and F agree within the error of D?

Error analysis:  Uncertainty in C from uncertainty in slope and i, or uncertainty in slope and R

All calculations are of the form f = x/y.

(13) inside back cover:   fractional error in f = ( ( sx/x)2 + (sy/y) 2 )1/2 .

C = i/ slope;    i => x,   slope => y

Example:

1% error in i => 				sx/x = 0.01

1.5 % error in slope  => 			sy/y = 0.015

fractional error in C => (.012 + .0152 )1/2 = .001 (122 + 152)1/2 => 0.018  => 1.8% error in C