PH 235 Heat Capacity Experiment with Vernier Software Logger Pro 		rev 10/23/06

Plug the Labpro interface into the USB port of your laptop. The connector is in the middle on the right as you look right-side up at the Vernier lettering on the lab pro. There is a sliding door between the USB and serial port, so that either USB or serial may be used to connect.  Plug the wall cord into the wall and to the lab pro. Attach the force probe to the Labpro in Ch 1. Set the probe to the low range.  Make sure the force probe switch is on the Low Range. Double-click the Logger Pro 3.3 icon on your laptop to activate the program. (It is better to have all devices activated and attached before you launch Logger Pro, so the program can detect what hardware is present.)

On the top bar menu go to Setup, then go to Sensors. It should show a force sensor in Ch1 .

Now under Setup, go to Data Collection The mode should be Real Time Collect.

Set the sampling speed to 1 per second on the slider bar Set the Experiment Length to 30 seconds. This is the time for your initial checkout, and for the real experiment you will reset it to 360 sec.

As a test, mass one of the metals (any but lead) on the little electronic balance, press Collect. During the run, place the mass on the pan for a few seconds, then remove it. You should find the change in force reading equals the weight of the metal sample. When this works ok, then reset the experiment length to 360 sec.

Experiment.

Determine the mass in grams that you will be adding.  The cool little electronic scales can be used, except for lead, whose samples are more than 50 g. With your collecting cup in the pan and filled with liquid nitrogen (LN2), start collecting data and let it run for perhaps 100 sec, then gently place the mass in the cup. Let the mass stay in the cup until it stops boiling. (It gives a last burst of bubbles before it stops.). Gently remove your sample and let the experiment continue to the end. Sanity check: Examine the graph and check that the weight increased by roughly the right amount for your mass added. (This will be a double-check that you are on the right setting on the force probe.)

Save your data to two files. First do a Save as a .cmbl file. Then use Export Data and save it in text format (the text format file can be opened by excel, and the cmbl file can be reopened by Logger).  Do at least three metals of:   aluminum, copper lead, and iron. If time permits, do all four metals.

From the graph you want the mass of LN2 boiled off by cooling the metal, but not due to regular evaporation and heating from the room.

Bring up a graph in either Logger Pro or Excel. You should have two lines fairly parallel to one another for the boiling rate before and after adding and cooling and removing the metal sample.  (More on next page)

Rescale the graph so that all of both sloped lines are present, but not any additional stuff. The distance h should be as large as possible. (The dotted lines are extensions of the actual data.)

h

You want the vertical distance h on the graph with as much precision as you can get, so the graph must be rescaled in order to make h as large on the page as possible.  This is the difference in weight due to the LN2 being boiled off because of the metal being added and cooled.  This number, converted to grams, and coupled with the heat of vaporization of LN2, 47.23 cal/g, will give the number of calories absorbed by the LN2.

The specific heat data given here is to be used to find the average specific heat of each metal between 77 K and room temperature.

Fedata:=[[50,0.73],[70,1.61],[100,2.88],[150,4.33],[200,5.13],[250,5.63],[298,5.97]];

Aldata:=[[50,0.91],[70,1.85],[100,3.12],[150,4.43],[200,5.16],[250,5.56],[298,5.82]];

Cudata:=[[50,1.49],[70,2.62],[100,3.85],[150,4.90],[200,5.43],[250,5.72],[298,5.85]];

Pbdata:=[[50,5.10],[70,5.54],[100,5.84],[150,6.04],[200,6.18],[250,6.30],[298,6.41]];

This data is [T,C], where T is in kelvins, and C is in Cal/mol/K.

Plot the data and determine the average heat capacity of the metal between 77K and room temperature.

{The room temperature heat capacity is 3R = 5.96 cal/mol/K, so you would expect a little less when you have figured out the correct value, because you can see the value decreasing as we get to lower temperatures. } (A simple but not totally precise method is to put a rectangle on the graph where the area under the rectangle, measured by eye, is about the same as the area under the curve. )

Excel will give you a fairly smooth curve through the data using a polynomial fit to, say, 5th order. In order to numerically integrate this curve from 77 to 293 K you must get Excel to give you something  like 4 sig figs for each of the coefficients. To do this, right-click on the equation of the fit, and then select Format Data Labels. Then select the Number tab at the top, and then pick Scientific. Now you get to select 4 or so decimal places, and these will be visible in the equation of the fit.

Suppose the average for aluminum came out to be 4.5 cal/mol/K over the range from 77 to 293 K. If we had 27 g of Al, it would be one mole and the aluminum would lose 4.5 * 1 * 216 = 972 cal in cooling from room temperature to 77 K.

Make a table of the heat gained by LN2 for each metal, and the calculated amount of heat lost by the metal in cooling to 77K.  Make it clear how you obtained your values, and show a sample calculation for heat gained and heat lost.

If your results are way, way off (like 400%) your force sensor may have gotten out of whack. The force graph can tell you about how much mass you added (and then later removed). Use this additional mass (of iron, or copper, or whatever) on the graph to see if it checks with the known mass that you added. If the graph says you added 4 times the known mass, then it got confused. Use the known mass and the graph to correct the values of weight lost in the liquid nitrogen.