# Niusha Rostamkolai

Box 115

# AC Circuits

ECE 204

HW #26

Problems:

1     _____

2     _____

- A 25 kVA, 2400/240 V, 60 Hz distribution transformer was tested at 60 Hz, and

the following data were obtained:

| Parameters | Open Circuit Test - LV Side | Short Circuit Test - HV Side |
| --- | --- | --- |
| Voltage (V) | 240 | 55 |
| Current (A) | 3.2 | 10.4 |
| Power (W) | 165 | 375 |

Compute the efficiency for full-load output at rated voltage and 0.8 power factor

lagging.

- A 50 kVA 2400/240 V single-phase transformer was tested and the following data

were obtained:

| Parameters | Open Circuit Test - LV Side | Short Circuit Test - HV Side |
| --- | --- | --- |
| Voltage (V) | 240 | 55 |
| Current (A) | 5.0 | 20.8 |
| Power (W) | 450 | 600 |

- Compute the voltage regulation and efficiency when the transformer is connected

to a load that takes 156 A at 220 V and 0.8 power factor lagging.

- Compute the voltage regulation and efficiency at the rated conditions and 0.8

power factor lagging.