ECE 452

PSpice Project 4

Three-Phase Half-Wave & Full-Wave Bridge Rectifiers

Objective

The objective of this project is to become familiar with the performance of three-phase half-wave and full-wave bridge rectifiers.

Procedure

Implement circuits of Figures 1 and 2 in PSpice. The sinusoidal source (Vsin) has an rms voltage of 120 V and a frequency of 60 Hz. The load has a resistance of 5 . Diodes have the following characteristics:

Reverse breakdown Voltage = 1600 V

Reverse breakdown Current = 20 mA

Reverse Saturation Current  = 250 A

Figure 1. Half-Wave Rectifier                          Figure 2. Full-Wave Rectifier

- Plot the three-phase input voltages and currents on one graph as subplot 1, and output voltage and current on one graph as subplot 2 from 0 to 50 ms for the three-phase half-wave rectifier of Figure 1:

- Calculate Fourier components of the output voltage with the PSpice.

- Add a series inductance of 5 mH to the load. Plot the three-phase input voltages and currents on one graph as subplot 1, and output voltage and current on one graph as subplot 2 from 0 to 50 ms for the three-phase half-wave rectifier of Figure 1:

- Calculate Fourier components of the output voltage with the PSpice.

- Plot the three-phase input voltages and currents on one graph as subplot 1, and output voltage and current on one graph as subplot 2 from 0 to 50 ms for the three-phase full-wave bridge rectifier of Figure 2:

- Calculate Fourier components of the output voltage with the PSpice.

- Add a series inductance of 5 mH to the load. Plot the three-phase input voltages and currents on one graph as subplot 1, and output voltage and current on one graph as subplot 2 from 0 to 50 ms for the three-phase full-wave bridge rectifier of Figure 2:

a.   Calculate Fourier components of the output voltage with the PSpice.

Report

Write a memo and discuss and compare the results. Attach the PSpice output files and all of your hand calculations to your memo.