ECE 452

PSpice Project 5

DC Converters

Objective

The objective of this project is to become familiar with the performance of a buck converter/chopper.

Procedure

Implement the IGBT buck chopper, shown in Figure 1, in the PSpice. The dc input voltage Vs is 100 V, and the load consists of a 5  resistor in series with a 5 mH inductor. The filter inductance is 3 mH and its capacitance is 160 F. Select the PSpice IGBT model and an ideal diode model for the freewheeling diode, both from the Class Library. The chopper operating frequency is 1 kHz, and its duty cycle is 40%.

Figure 1. Circuit Diagram of Buck Chopper

Design the triggering circuit, and simulate the response of this chopper for 40 ms. Perform the following tasks:

- Plot the triggering pulse voltage and Vce of the IGBT on one graph from 0 to

5 ms. Use this to confirm that the IGBT is turned on and off at the right time.

b. Plot the source and the load currents on one graph from 0 to 40 ms and 30 to

40 ms.

c. Plot the negative of diode voltage (VAK), and the load voltage on one graph from

0 to 40 ms and 30 to 40 ms.

d. Calculate the average output voltage by hand and compare it with the simulation

result.

e. By re-designing the LC filter, improve the peak-to-peak load ripple voltage such

that it is less than 2 V. To verify your design, plot the load voltage and indicate

the filter parameter values on the plot. Make sure that values of L and C are

realistic. Plots should be from 0 to 40 ms and 30 to 40 ms.

f. Use the re-designed LC filter of Part e and increase the duty cycle to 80%. Repeat 	  	    the simulation and plot the source and the load currents on one graph from 0 to 40

ms and 30 to 40 ms.

g. Also, plot the negative of diode voltage (VAK), and the load voltage on one graph

from 0 to 40 ms and 30 to 40 ms.

Report

Write a memo and discuss the results. Attach the PSpice input files and all of your hand calculations to your memo.