ECE 452

PSpice Project 7

Single-Phase Inverters

Objective

The objective of this project is to become familiar with the performance of a single-phase bridge inverter.

Procedure

Implement the single-phase bridge inverter, shown in Figure 1, in the PSpice. Use the IGBT and ideal diode models from the class library. The dc input voltage  Vs is 190 V, and the load is a 20  resistor. The output frequency is 60 Hz.

Figure 1. Circuit Diagram of a Single-Phase Inverter

Design the triggering circuit, and simulate the response of this inverter for 50 ms. Perform the following tasks:

a. Plot gate voltages on one sheet as two subplots

b. Plot output voltage and current on one sheet as two subplots

c. Plot input voltage and current on one sheet as two subplots

d. Perform the harmonic analysis of output voltage and current with Pspice and by

hand. Compare the results by Excel Bar Charts.

Change the load to a series resistor and inductor. The load resistance is 20 ohms, and the load inductance is 0.2 H. Perform the following tasks for 50 ms:

a. Plot gate voltages on one sheet as two subplots

b. Plot output voltage and current on one sheet as two subplots

c. Plot input voltage and current on one sheet as two subplots

d. Perform the harmonic analysis of output voltage and current with Pspice and by

hand. Compare the results by Excel Bar Charts.

Report

Write a memo and discuss the results. Attach the PSpice input files and all of your hand calculations to your memo.