## Slide 1
Your First Robot program
For the Create robot
In Python
Based on the create module (library), originally developed by Zach Dodds at Harvey Mudd
import new_create
import time
def main():
port = 4
robot = new_create.Create(port)
robot.go(10, 90)
time.sleep(4.0)
robot.stop()
sensor = new_create.Sensors.distance
v = robot.getSensor(sensor)
print(v)
robot.shutdown()
Start the robot moving:
  At 10 cm/sec forwards
  While spinning 90 degrees/sec counterclockwise
Sleep 4 seconds (while the above motion continues), then stop.
Always have your program execute this at its end!
Connects to a Create robot using the given COM port
Specify a sensor (here, the distance sensor that says how far the robot has moved linearly since you last asked), then get and print the current value of the sensor.