## Slide 1: Introductory - PIC 101 Introduction to PIC® MCUs Hands-on Workshop

## Slide 2: Why am I here?

## Slide 3: In this workshop you will have a chance to:
Explore different application areas where microcontrollers are used
Develop a real world working application
Work with Microchip’s development tools
  PICSTART Plus programmer
  MPLAB software/application development manager
  Workshop board

## Slide 4: What you will do...continued
Develop application code
Test your design
  Workshop board
  Scale model prototype
Develop higher order functions
Evaluate your design on a workshop board

## Slide 5: Agenda Day 1
Review of architecture and instruction set
Break
Basic tools usage
Lunch
Switching
Timing
Break
Timing (continued)
Motor/motion control

## Slide 6: Agenda Day 2
Motor/motion control (continued)
Sensing inputs
Break
Sensing inputs (continued)
State logic and higher order functions
Lunch
State logic and higher order functions (continued)
Break
Proof on scale model prototype

## Slide 7: Why Microchip?
High reliability
Feature creep solution
Speed of implementation
Development tools suite
Lower cost
Field upgrades

## Slide 8: Final project goal
Automatic door controller (commercial type)
Notes: Declare the final project goal. There are 2 pictures of commercial applications. One on this slide and one on the next. One is grocery store type, one is office type.

## Slide 9: What feature set?
Notes: Use flip chart and have class call out list of features the door should have. Then show next slide with the list you came up with. This slide is not in student handbook.

## Slide 10: What feature set
  Open/close
  Switch controlled
  Held open to allow passage through door
  Automatic close (store type)
  Safety cutoffs (if time permits)
  Independent motor cutoff (if time permits)
  Double tap (if time permits)
  Lighting control (optional)
  Sound control (optional)
Notes: Note to students that on your list, the optional items do not refer to the actual project they will be doing.

## Slide 11: Microcontroller applications involved
Switching
Timing
Movement/motor control
Sensing
State decisions/logic
Notes: Give examples in the mechanical world of each of these sections as instructor feels fit. Throw switch circuit breaker Vs electrical switch in PIC. Egg timer Vs. Tmr0 watchdog timer . Pullys gears Vs applying voltage to drive motor. Finger probes mechanical vs opto sensors pressure sensors .

## Slide 12: Lab Notes
There are 10 labs covering different microcontroller application areas
Write code by modules (towards final project)
Notes: Explain that they should write code modules. It makes the later projects easier as they can re-use code.

## Slide 13: PIC 101
Architecture

## Slide 14: PIC Architecture RISC-like Features
Harvard architecture
Register file concept
All instructions single-word
LWI (Long Word Instruction)
Instruction pipelining
Single-cycle instructions
Reduced instruction set
Orthogonal instruction set
The high performance of the PIC MCU family can be attributed to the following architectural features:
Notes: Reduced Vs Complex instruction set intel 8051 (licensed)
Register as if they are files each have an address
more than 8 bits
Explain orthogonal as there is not a follow on slide covering it. The way you access registers simultaneously

## Slide 15: PIC Architecture Harvard Architecture
Fetches instructions and data from one memory.
  Limits Operating Bandwidth
Two separate memory spaces for instructions and data.
  Increases throughput
  Different program and data bus widths are possible
Program
and Data
Memory
Von Neumann
8-Bits
CPU
Program
Memory
Data
Memory
8-Bits
12/14/16-Bits
Harvard
CPU
Notes: Highlight advantages of the 2 bus methodology.

## Slide 16: PIC MCU Architecture Pipelining
Flush Fetch 4
Fetch SUB_1
In most microcontrollers, instructions are fetched and executed sequentially.
Allows overlap of fetch and execution.
Makes single cycle execution.
Program branches (e.g. GOTO, CALL or Write to PC) takes two cycles.
Tcy0 Tcy1 Tcy2 Tcy3 Tcy4
Execute 1
Fetch 3
1. MOVLW 55h
Fetch 1
Execute 3
Fetch 2
Execute 2
Fetch 4
2. MOVWF PORTB
3. CALL SUB_1
4. BSF PORTA, BIT3
Notes: Cover basic pipeline. Also cover branch conditions and the number of instruction cycles needed for branch taken and branch not taken.

## Slide 17: PIC MCU Architecture Block Diagram
Program
Bus
EPROM
Program
Memory
Clock/Counter
T0CKI
I/O Ports
Ports
Peripheral(s)
Instruction
Decode &
Control
Timing
Generation
MCLR
OSC1
OSC2
Watchdog
Timer
Power-on
Reset
OSC Start
-upTimer
Brown-out
Reset
Program Counter
STACK1
STACKn
STATUS Reg
Mux
W Reg
ALU
MOVF PORTB,W
00100000000110
001000 0 0000110
001000 0
0000110
01010101
01010101
Direct Addr
Addr Mux
RAM
File Registers
Data Bus
Instruction Reg
Indirect Data
Address
FSR
MOVLW 0xAA
11000010101010
MOVF INDF,W
00100000000000
10101010
110000 10101010
001000 0 0000000
000000
110000
001000 0

## Slide 18: PIC Architecture Register File Concept
General Purpose
Registers (RAM)
Other SFRs
PORTA
FSR
STATUS
PCL
TMR0
INDF
W Register
ALU
Data
Memory
Direct data addr <7>
Op code <7>
14-bit Instruction Format Example:
RAM is a bank of general purpose registers.
Peripherals (I/O) are registers.
All instructions operate on any register.
Long word instruction allows direct addressing of registers.
Notes: Highlight register files. Pull examples from data sheets as needed.

## Slide 19: Quiz 1
1) All of Microchip’s PIC instructions are _____.
2) The PIC pipeline must be flushed whenever ____ is modified.
Single Cycle
Single Byte
Single Word
W register
PortB
PC
Notes: Let students work on quiz for 5 min. then review as a group calling on individuals for answers. (interact)
1)word
2)pc

## Slide 20: PIC Architecture
Memory

## Slide 21: PIC Architecture Memory
2 types of memory
  Program
  Data
Organization
  Pages (program)
  Banks (data)
Notes: Explain that mapping methodology used due to limited number of bits available.

## Slide 22: PIC Architecture Paging / Banking Boundary Summary
PIC16/17
Family
Word
Size
(Bits)
Code
Page
Boundary
(Words)
Current
Max code
Size
(Words)
Register
Bank
Boundary
(Bytes)
Current
Max RAM
Size
(Bytes)
16F5X
12
512
2K
32
73
16FXXX
14
2048
8K
128
368
17CXXX
16
8192
16K/64K
256
902
Notes: Show how each of the cores relates to the different page and bank schemes. Point out that when go thru instruction set the number of bits available for addressing is shown.

## Slide 23: PIC16FXX Architecture Program Memory
Maximum 8K Bytes (13 bits) of program memory space
Four Pages each 2K bytes (11 bits)
Page access using PCLATH<4:3>
Reset Vector at 0000h
Interrupt Vector at 0004h
Page 0
0000h
0004h
07FFh
Interrupt
Reset
Page 1
0800h
0FFFh
Page 2
1000h
17FFh
Page 3
1800h
1FFFh
PCLATH<4:3> = 00
PCLATH<4:3> = 01
PCLATH<4:3> = 10
PCLATH<4:3> = 11
Notes: <number>
<footer>
<header>
<date/time>
Reset vector at 0, Interrupt vector at 4h
In 2K Program memory, PCLATH has no impact
In 4K Program memory, PCLATH bit 3 selects 2K page. Since PCLATH is not ininialized on reset (POR or otherwise), user must initialize PCLATH after reset.

## Slide 24: PIC Architecture Paging program memory
Paging needs consideration ONLY when executing program CALL or GOTO operation
Modify page bits ONLY when jumping to different page than last jumped
  page bits define desired page execution
Instructions invoking page bits:
  GOTO <address>
  CALL <address>
  <Instruction> PCL,F ; e.g. ADDWF PCL,F
There are no paging considerations when returning
Notes: For this slide and next 4, refer to data sheets as needed to clarify and get them use to looking in DS for the different data.
Ask Why the last bullet is true.
Answer: Because the Stack is full width.

## Slide 25: PIC Architecture Paging program memory
ADDWF PCL,F has eight bits (256 words) of address
  In PIC16F5X PA0, PA1 determine final page
    Bit 8 of PC is cleared by hardware
    Destination address must be first 256 of page
  In PIC16FXXX/17CXXX, PCLATH is used for upper address
    Destination address can be anywhere
    Look-up tables that cross a 256 word boundary require pre-conditioning of PCLATH
Notes: 5x is a x12 core tell them how the x12 is acceses pages versus how the 16c/17c acceses the pages.

## Slide 26: PIC Architecture Paging program memory
PC
12
8
7
0
5
PCLATH<4:0>
PCLATH
INST with PCL
as dest
ALU result
GOTO, CALL
Opcode <10:0>
8
PC
12
11
10
0
11
PCLATH<4:3>
PCH
PCL
8
7
2
PCLATH
PCH
PCL
PIC16F84A
PA1:PA0
2
STATUS
PC
8
7
0
PCL
9
10
PA1:PA0
2
STATUS
PC
8
7
0
PCL
9
10
Instruction Word
Reset to ‘0’
Instruction Word
7
0
7
0
GOTO Instruction
CALL or Modify PCL Instruction
PIC16F57
Notes: Tell students that on 12 bit core the page bits are pulled from status.
On 14 bit core the page bits come from pclath.

## Slide 27
PC<12:0>
Stack Level 1



Stack Level 8
Reset Vector
Peripheral Interrupt Vector
User Memory
Space
CALL, RETURN
RETFIE, RETLW
13
0000h
0004h
1FFFh
3FFh
PIC16F57
Program Memory Map
PIC16F84A
PC<10:0>
Stack Level 1
Stack Level 2
User Memory
Space
11
000h
1FFh
Reset Vector
0FFh
100h
On-chip Program
Memory (Page 0)
On-chip Program
Memory (Page 1)
On-chip Program
Memory (Page 2)
On-chip Program
Memory (Page 3)
200h
3FFh
2FFh
300h
400h
5FFh
4FFh
500h
600h
7FFh
6FFh
700h
CALL, RETLW
Notes: 0 to 3ff on The x12 has 1 page boundries on the x14 there arent any page boundries. Why? Because you have 2 more bits.

## Slide 28
PIC Architecture Program Memory: Immediate Operation
  8-bit constant (literal) value included in
    instruction word.
  Used by literal instructions such as
  movlw, addlw, retlw, etc.
OP CODE
k
14-bit Instruction for Literal Instructions
k
k
k
k
k
k
k
Notes: Paging where do I get the extra bits I need

## Slide 29
PIC Architecture Program Memory: PC Absolute Addressing
OP CODE
k
k
k
k
14-bit Instruction for call and goto
k
k
k
k
k
k
k
  Used by control instructions CALL and GOTO
  to modify the PC (Program Counter)
k
k
k
k
k
k
k
k
k
x
x
x
k
k
x
x
x
PCLATH Register
Effective 13-bit Program Memory Address
11-bits From Instruction
2-bits
From
PCLATH
k
k
k
k
Notes: How many bits doesit take to address 8K of Program Memory?

## Slide 30
PIC Architecture PC Relative Addressing (14-bit core)
PCH <5>
PCL <8>
13-Bit Program Counter
PCLATH <5>
Internal Data Bus <8>
5
5
8
  First write high byte to PCLATH.
  Next write low byte to PCL, this loads the entire
13-bit value to PC.
movlw HIGH Delay
movwf PCLATH
movlw LOW Delay
movwf PCL
Note: PCH cannot be read
Notes: Tricky way to get the bits you need to address 8K

## Slide 31
00000000
XXXXXXXX
PIC MCU Architecture PC Relative Addressing
Look-up Table Example
movlw HIGH Decode
movwf PCLATH
movf DisplayValue,W
call Decode
movwf PORTB
goto Continue
Decode
addwf PCL,F
retlw B’00111111’ ;decode 0
retlw B’00000110’ ;decode 1
retlw B’01011011’ ;decode 2
retlw B’01001111’ ;decode 3
retlw B’01100110’ ;decode 4
retlw B’01101101’ ;decode 5
retlw B’01111101’ ;decode 6
retlw B’00000111’ ;decode 7
retlw B’01111111’ ;decode 8
retlw B’01101111’ ;decode 9
Continue
b
e
g
a
f
d
c
RB0
RB1
RB2
RB3
RB4
RB5
RB6
b
c
d
e
f
g
W Register
I/O Port B
01101101
00000101
movf DisplayValue,W
call Decode
addwf PCL,F
retlw B’01101101’ ;decode 5
movwf PORTB
01101101
g
a
f
d
c
b
e

## Slide 32: PIC16FXX Architecture Data Memory
Four banks each of 128 bytes of Data Memory
Special Function Registers (SFRs) are mapped in top 32 locations
Banks selected by RP0,1 and IRP in Status register
GPRs
SFRs
Bank0
000h
01Fh
020h
07Fh
GPRs
SFRs
Bank1
080h
09Fh
0A0h
0FFh
0F0h
GPRs
SFRs
Bank2
100h
11Fh
120h
17Fh
170h
GPRs
SFRs
Bank3
180h
19Fh
1A0h
1FFh
1F0h
RP<1:0> RP<1:0> RP<1:0> RP<1:0>
= 00 = 01 = 10 = 11
Notes: <number>
<footer>
<header>
<date/time>
RP1 and IRP should not be used as GP bits, in order to maintain upward compatibility.
RP0 selects between bank 0 and bank 1.
A “r/w” to bank 2 and 3 will be a “r/w” to bank 0 or 1 depending on the state of RP0.
Explain due to number of bits available banking is a efficient way to get more memory.
Same as program memory limitations in # of bits thus 4 banks.
What are the shaded in yellow and what are they usefull for?

## Slide 33: PIC Architecture Methods for accessing data memory
Direct
Indirect

## Slide 34: PIC Architecture Data Memory: Direct Addressing
7-bit direct address from the instruction
2-bits from STATUS register
Effective 9-bit Register Address
IRP
RP1
RP0
OP CODE
TO
PD
Z
DC
C
STATUS Register
14-bit Instruction
f
f
f
f
f
f
f
RP1
RP0
f
f
f
f
f
f
f
7-bits From Instruction Word
2-bits From
STATUS
Register

## Slide 35: PIC Architecture Data Memory: Indirect Addressing
IRP
f
f
f
f
f
f
f
f
f
8-bit indirect address from the FSR (File Select Register).
1-bit from STATUS register.
IRP
RP1
RP0
TO
PD
Z
DC
C
f
f
f
f
f
f
f
STATUS Register
8-bit FSR Register
Effective 9-bit Register Address
8-bits From FSR
1-bit From
STATUS
Register

## Slide 36: PIC Architecture Data Memory: Indirect Addressing
      Clear all RAM locations from 0x20 to 0x7F.
      Indirect address is loaded into FSR.
      Every time INDF is used as operand, register pointed to by FSR is actually used.
movlw 0x20
movwf FSR
LOOP clrf INDF
incf FSR,F
btfss FSR,7
goto LOOP
<next instruction>
0000 0000
0000 0000
FSR = 20h
INDF
00h
04h
20h
7Fh
Data Memory

## Slide 37: PIC Architecture Data memory map
File Address
00
h
01
h
02
h
03
h
04
h
05
h
06
h
07
h
08
h
09
h
0A
h
0B
h
0C
h
7F
h
80
h
81
h
82
h
83
h
84
h
8
5h
86
h
87
h
88
h
89
h
8A
h
8B
h
8
Ch
FF
h
Bank 0
Bank 1
Indirect addr.
(1)
Indirect addr.
(1)
TMR0
OPTION
_REG
PCL
STATUS
FSR
PORTA
PORTB
EEDATA
EEADR
PCLATH
INTCON
68
General
Purpose
Registers
SRAM)
PCL
STATUS
FSR
TRISA
TRISB
EECON1
EECON2
(1)
PCLATH
INTCON
Mapped
in Bank 0
Unimplemented data memory location; read as '0'.
File Address
Not a physical register.
CFh
D0h
4Fh
50h
(accesses)
Register File Map
PIC16F84A
Notes: Note to students that 508 ds shows no bank 1.

## Slide 38: Quiz 2
1) What bits must you set prior to calling a subroutine?
2) What bits must you set prior to returning from a subroutine?
3) Data tables in program memory do not need to have page bits set.
Both
Page
Bank
Neither
Both
Page
Bank
Neither
True
False
Notes: Let students work on this for 5 min. then review with them like quiz 1.
1)page
2)neither
3)false

## Slide 39: Quiz2 (cont.)
4) For the 12-bit core, what SFR register and respective bits are needed to access different pages in program memory ?
5) For the 14-bit core, what SFR register and respective bits are needed to access different pages in program memory?
6) What bits are needed to access different RAM banks?
___________________________________________________________________________
___________________________________________________________________________
1)________________________2)________________________3)________________________4)________________________
Notes: 4)PA1 & PA0, Opcode itself, PC
5)PCLATH <4:3>, Opcode itself, PCL
6)Direct: RP<1:0>, Opcode itself,
Indirect IRP, FSR

## Slide 40: PIC MCUs
Instruction Set

## Slide 41: PIC MCU Instruction Set
33 instructions  12-bit core
35 instructions  14-bit core
58 instructions  16-bit core
  Easy to learn
  High compaction
  Very powerful single-word instructions
  All single-cycle except program branches
  Upward compatibility of instructions
Notes: Talk about the RISC and how since instruction set is small, code is portable to other parts.

## Slide 42: 12-bit Core Instruction Set: Instruction Set Summary
Byte-Oriented Operation
NOP - No Operation - 0000 0000 0000
MOVWF f Move W to f W  f 0000 001f ffff
CLRW - Clear W 0  W 0000 0100 0000
CLRF f,d Clear f 0  f 0000 011f ffff
SUBWF f,d Subtract W from f f - W  d[f+W+1  d] 0000 10df ffff
DECF f,d Decrement f f - 1  d 0000 11df ffff
IORWF f,d Inclusive OR W and f W v f  d 0001 00df ffff
ANDWF f,d AND W and f W & f  d 0001 01df ffff
XORWF f,d Exclusive OR W and f W  f  d 0001 10df ffff
ADDWF f,d Add W and f W + f  d 0001 11df ffff
MOVF f,d Move f f  d 0010 00df ffff
COMF f,d Complement f f  d 0010 01df ffff
INCF f,d Increment f f + 1  d 0010 10df ffff
DECFSZ f,d Decrement f, skip if zero f - 1  d, skip if zero 0011 11df ffff
RRF f,d Rotate right f f(n)  d(n-1), f(0)  C, C  d(7) 0011 00df ffff
RLF f,d Rotate left f f(n)  d(n+1), f(7)  C, C  d(0) 0011 01df ffff
SWAPF f,d Swap halves f f(0:3)  f(4:7)  d 0011 10df ffff
INCFSZ f,d Increment f, skip if zero f + 1  d, skip if zero 0011 11df ffff
Legends: f = file address <5>; b = bit address <3>; k = literal or immediate value (8 or 9 bit);
d = destination select; d = 0: W reg, d = 1: f

## Slide 43: 12-bit Core Instruction Set: Instruction Set Summary (Cont.)
Bit-Oriented Operations
BCF f,b Bit clear f 0 f(b) 0100 bbbf ffff
BSF f,b Bit set f 1 f(b) 0101 bbbf ffff
BTFSC f,b Bit test f, skip if clear Test bit (b) in file (f), skip if clear 0110 bbbf ffff
BTFSS f,b Bit test f, skip if set Test bit (b) in file (f), skip if set 0111 bbbf ffff
Literal and Control Operations
OPTION - Load OPTION register W  OPTION register 0000 0000 0010
SLEEP - Go into Standby Mode 0  WDT, stop oscillator 0000 0000 0010
CLRWDT - Clear Watchdog Timer 0  WDT 0000 0000 0100
TRIS f Tri-state™ Port f W  I/O control register f 0000 0000 0fff
RETLW k Return, place Literal in W k  W, Stack PC 1000 kkkk kkkk
CALL k Call Subroutine PC + 1 Stack, k PC 1001 kkkk kkkk
GOTO k Go to address (k is 9 bit) k PC (9 bits) 101k kkkk kkkk
MOVLW k Move Literal to W k W 1100 kkkk kkkk
IORLW k Inclusive OR Literal and W k v W W 1101 kkkk kkkk
ANDLW k AND Literal W k & W W 1110 kkkk kkkk
XORLW k Exclusive OR Literal W K  W W 1111 kkkk kkkk
Legends: f = file address <5>; b = bit address <3>; k = literal or immediate value (8 or 9 bit);
d = destination select; d = 0: W reg, d = 1: f

## Slide 44
PIC Instruction Set 14-bit core Summary
NOP - No Operation
MOVWF f Move W to f
CLRW - Clear W
CLRF f Clear f
SUBWF f,d Subtract W from f
DECF f,d Decrement f
IORWF f,d Inclusive OR W and f
ANDWF f,d AND W and f
XORWF f,d Exclusive OR W and f
ADDWF f,d Add W and f
MOVF f,d Move f
COMF f,d Complement f
INCF f,d Increment f
DECFSZ f,d Decrement f, skip if zero
RRF f,d Rotate right f through carry
RLF f,d Rotate left f through carry
SWAPF f,d Swap nibbles of f
INCFSZ f,d Increment f, skip if zero
BCF f,b Bit clear f
BSF f,b Bit set f
BTFSC f,b Bit test f, skip if clear
BTFSS f,b Bit test f, skip if set
SLEEP - Go into standby mode
CLRWDT - Clear watchdog timer
RETLW k Return, place literal in W
RETFIE - Return from interrupt
RETURN - Return from subroutine
CALL k Call subroutine
GOTO k Go to address (k is 9-bit)
MOVLW k Move literal to W
IORLW k Inclusive OR literal with W
ADDLW k Add literal with W
SUBLW k Subtract W from literal
ANDLW k AND literal with W
XORLW k Exclusive OR literal with W
Byte-Oriented Operations
Bit-Oriented Operations
Literal and Control Operations
f = File Register, k = literal value (8-bit), b = bit address <0,7>, d = destination (0=W, 1=f)

## Slide 45
PIC Instruction Set Byte-Oriented Operations
14-bit Instruction for Byte Oriented Operations
OP CODE
d
f
f
f
f
f
f
f
d = Destination Bit
d = 0 for destination W
d = 1 for destination f
f = 7-bit Register Address
Example:
ADDWF REG, W
ADDWF f, d
NOP -
MOVWF f
CLRW -
CLRF f
SUBWF f,d
DECF f,d
IORWF f,d
ANDWF f,d
XORWF f,d
ADDWF f,d
MOVF f,d
COMF f,d
INCF f,d
DECFSZ f,d
RRF f,d
RLF f,d
SWAPF f,d
INCFSZ f,d
Byte-Oriented
Operations

## Slide 46
PIC MCU Instruction Set Byte-Oriented Operations
NOP No Operation
Syntax: NOP
Operands: None
Operation: No operation
Status: None
Encoding: 00 0000 0000 0000
Words: 1
Cycles: 1
Example:
NOP

## Slide 47
PIC MCU Instruction Set Byte-Oriented Operations
MOVWF Move W to f
Syntax: MOVWF f
Operands: 0 <= f <= 127
Operation: (W) -> (f)
Status: None
Encoding: 00 0000 1fff fff
Words: 1
Cycles: 1
Example:
MOVWF FSR
Before Instruction
FSR = 0xFF
W = 0x4F
After Instruction
FSR = 0x4F
W = 0x4F

## Slide 48
PIC MCU Instruction Set Byte-Oriented Operations
CLRW Clear W
Syntax: CLRW
Operands: None
Operation: 00h -> (W)
1 -> Z
Status: Z
Encoding: 00 0001 0000 0000
Words: 1
Cycles: 1
Example:
CLRW
Before Instruction
W = 0x4F
After Instruction
W = 0x00
Z = 1

## Slide 49
PIC MCU Instruction Set Byte-Oriented Operations
CLRF Clear f
Syntax: CLRF f
Operands: 0 <= f <= 127
Operation: 00h -> (f)
1 -> Z
Status: Z
Encoding: 00 0001 1fff ffff
Words: 1
Cycles: 1
Example:
CLRF FSR
Before Instruction
FSR = 0x4F
After Instruction
FSR = 0x00
Z = 1

## Slide 50
PIC MCU Instruction Set Byte-Oriented Operations
SUBWF Subtract W from f
Syntax: SUBWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - (W) -> dest
Status: C,DC,Z
Encoding: 00 0010 dfff ffff
Words: 1
Cycles: 1
Example:
SUBWF FSR,W
Before Instruction
FSR = 0x03
W = 0x02
C = ?
Z = ?
After Instruction
FSR = 0x03
W = 0x01
C = 0
Z = 0

## Slide 51
PIC MCU Instruction Set Byte-Oriented Operations
DECF Decrement f
Syntax: DECF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - 1 -> dest
Status: Z
Encoding: 00 0011 dfff ffff
Words: 1
Cycles: 1
Example:
DECF FSR,F
Before Instruction
FSR = 0x01
Z = 0
After Instruction
FSR = 0x00
Z = 1

## Slide 52
PIC MCU Instruction Set Byte-Oriented Operations
IORWF Inclusive OR W & f
Syntax: IORWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W) .OR. (f) -> dest
Status: Z
Encoding: 00 0100 dfff ffff
Words: 1
Cycles: 1
Example:
IORWF CNT,W
Before Instruction
CNT = 0x13
W = 0x91
After Instruction
CNT = 0x13
W = 0x93
Z = 0

## Slide 53
PIC MCU Instruction Set Byte-Oriented Operations
ANDWF AND W with f
Syntax: ANDWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W).AND.(f) -> dest
Status: Z
Encoding: 00 0101 dfff ffff
Words: 1
Cycles: 1
Example:
ANDWF CNT,F
Before Instruction
CNT = B’00010111’
W = B’11000010’
After Instruction
CNT = B’00000010’
W = B’11000010’
Z = 0

## Slide 54
PIC MCU Instruction Set Byte-Oriented Operations
XORWF Exclusive OR W & f
Syntax: XORWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W).XOR.(f) -> dest
Status: Z
Encoding: 00 0110 dfff ffff
Words: 1
Cycles: 1
Example:
XORWF FSR,W
Before Instruction
FSR = B’10101111’
W = B’10110101’
After Instruction
FSR = B’10101111’
W = B’00011010’
Z = 0

## Slide 55
PIC MCU Instruction Set Byte-Oriented Operations
ADDWF Add W with f
Syntax: ADDWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W) + (f) -> dest
Status: Z
Encoding: 00 0111 dfff ffff
Words: 1
Cycles: 1
Example:
ADDWF FSR,W
Before Instruction
FSR = 0x17
W = 0xC2
After Instruction
FSR = 0x17
W = 0xD9
Z = 0

## Slide 56
PIC MCU Instruction Set Byte-Oriented Operations
MOVF Move f
Syntax: MOVF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) -> dest
Status: Z
Encoding: 00 1000 dfff ffff
Words: 1
Cycles: 1
Example:
MOVF FSR,F
Before Instruction
FSR = 0x00
Z = 0
After Instruction
FSR = 0x00
Z = 1

## Slide 57
PIC MCU Instruction Set Byte-Oriented Operations
COMF Complement f
Syntax: MOVF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) -> dest
Status: Z
Encoding: 00 1001 dfff ffff
Words: 1
Cycles: 1
Example:
COMF REG,W
Before Instruction
REG = 0x13
W = 0x58
Z = 0
After Instruction
REG = 0x13
W = 0xEC
Z = 0

## Slide 58
PIC MCU Instruction Set Byte-Oriented Operations
INCF Increment f
Syntax: INCF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) + 1 -> dest
Status: Z
Encoding: 00 1010 dfff ffff
Words: 1
Cycles: 1
Example:
INCF REG,F
Before Instruction
REG = 0xFF
Z = 0
After Instruction
REG = 0x00
Z = 1

## Slide 59
PIC MCU Instruction Set Byte-Oriented Operations
DECFSZ Dec. f, Skip if 0
Syntax: DECFSZ f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - 1 -> dest
skip if result = 0
Status: None
Encoding: 00 1011 dfff ffff
Words: 1
Cycles: 1(2)
Example:
Loop DECFSZ CNT,F
GOTO Loop
Continue
Before Instruction
PC = address Loop
After Instruction
CNT = CNT - 1
if CNT = 0,
PC = address Continue
if CNT != 0,
PC = address Loop+1

## Slide 60
PIC MCU Instruction Set Byte-Oriented Operations
RRF Rotate Right f -> C
Syntax: RRF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation:
Status: C
Encoding: 00 1100 dfff ffff
Words: 1
Cycles: 1
Example:
RRF CNT,W
Before Instruction
CNT = 1110 0110
C = 0
After Instruction
CNT = 1110 0110
W = 0111 0011
C = 0
C
Register f

## Slide 61
PIC MCU Instruction Set Byte-Oriented Operations
RLF Rotate Left f -> C
Syntax: RLF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation:
Status: C
Encoding: 00 1101 dfff ffff
Words: 1
Cycles: 1
Example:
RLF CNT,W
Before Instruction
CNT = 1110 0110
C = 0
After Instruction
CNT = 1110 0110
W = 1100 1100
C = 1
C
Register f

## Slide 62
PIC MCU Instruction Set Byte-Oriented Operations
SWAPF Swap Nibbles in f
Syntax: SWAPF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: f<3:0> -> dest<7:4>
f<7:4> -> dest<3:0>
Status: None
Encoding: 00 1110 dfff ffff
Words: 1
Cycles: 1
Example:
SWAPF REG,W
Before Instruction
REG = 0xA5
After Instruction
REG = 0xA5
W = 0x5A

## Slide 63
PIC MCU Instruction Set Byte-Oriented Operations
INCFSZ Inc. f, Skip if 0
Syntax: INCFSZ f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) + 1 -> dest
skip if result = 0
Status: None
Encoding: 00 1111 dfff ffff
Words: 1
Cycles: 1(2)
Example:
Loop INCFSZ CNT,F
GOTO Loop
Continue
Before Instruction
PC = address Loop
After Instruction
CNT = CNT + 1
if CNT = 0,
PC = address Continue
if CNT != 0,
PC = address Loop+1

## Slide 64
PIC MCU Instruction Set Bit-Oriented Operations
14-bit Instruction for Bit Oriented Operations
OP CODE
b
f
f
f
f
f
f
f
b = 3-Bit Address
(Bit Number)
f = 7-bit Register Address
b
b
Example:
BTFSC STATUS, C
BTFSC f, b
BCF f,b
BSF f,b
BTFSC f,b
BTFSS f,b
Bit-Oriented
Operations

## Slide 65
PIC MCU Instruction Set Bit-Oriented Operations
BCF Bit Clear f
Syntax: BCF f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: 0 -> (f<b>)
Status: None
Encoding: 01 00bb bfff ffff
Words: 1
Cycles: 1
Example:
BCF FSR,4
Before Instruction
FSR = 0011 0000
After Instruction
FSR = 0010 0000

## Slide 66
PIC MCU Instruction Set Bit-Oriented Operations
BSF Bit Set f
Syntax: BSF f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: 1 -> (f<b>)
Status: None
Encoding: 01 01bb bfff ffff
Words: 1
Cycles: 1
Example:
BSF FSR,4
Before Instruction
FSR = 0010 0000
After Instruction
FSR = 0011 0000

## Slide 67
PIC MCU Instruction Set Bit-Oriented Operations
BTFSC Bit Test f, Skip if 0
Syntax: BTFSC f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: skip if (f<b>) = 0
Status: None
Encoding: 01 10bb bfff ffff
Words: 1
Cycles: 1(2)
Example:
Here BTFSC CNT,1
False GOTO Done
True
Before Instruction
PC = address Here
After Instruction
if CNT<1> = 0,
PC = address True
if CNT<1> = 1,
PC = address False

## Slide 68
PIC MCU Instruction Set Bit-Oriented Operations
BTFSS Bit Test f, Skip if 1
Syntax: BTFSS f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: skip if (f<b>) = 1
Status: None
Encoding: 01 11bb bfff ffff
Words: 1
Cycles: 1(2)
Example:
Here BTFSS CNT,1
False GOTO Done
True
Before Instruction
PC = address Here
After Instruction
if CNT<1> = 1,
PC = address True
if CNT<1> = 0,
PC = address False

## Slide 69: PIC MCU Instruction Set Example: Bit Manipulation
XMIT: MOVLW 0x08 ;Bit count = 8
MOVWF bit_count
XM_LOOP:
BCF PORTB,DT ;preset clock & data lines to 0
BCF PORTB,CLK ;preset clock & data lines to 0
RRF XDATA,F ;rotate data right thru Carry
BTFSC STATUS,C ;test carry bit
BSF PORTB,DT ;set 1  Data pin
BSF PORTB,CLK ;set 1  Clock pin
DECFSZ bit_count,F ;decrement count
GOTO XM_LOOP ;Not done then repeat
BCF PORTB,CLK ;clear clock line and exit
Synchronous serial transmission of eight bits of data from file register XDATA to I/O Pin:
Clock
Data
0
1
7

## Slide 70
PIC MCU Instruction Set Literal Operations
k
14-bit Instruction for Literal Operations
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
Example:
MOVLW 0x2F
MOVLW k
MOVLW k
IORLW k
ADDLW k
SUBLW k
ANDLW k
XORLW k
Literal
Operations

## Slide 71
PIC MCU Instruction Set Literal Operations
MOVLW Move Literal to W
Syntax: MOVLW k
Operands: 0 <= k <= 255
Operation: k -> (W)
Status: None
Encoding: 11 0000 kkkk kkkk
Words: 1
Cycles: 1
Example:
MOVLW 0x5A
After Instruction
W = 0x5A

## Slide 72
PIC MCU Instruction Set Literal Operations
IORLW Inclusive OR Literal with W
Syntax: IORLW k
Operands: 0 <= k <= 255
Operation: (W) .OR. k -> (W)
Status: Z
Encoding: 11 1000 kkkk kkkk
Words: 1
Cycles: 1
Example:
IORLW B’00110101’
Before Instruction
W = B’10001010’
After Instruction
W = B’10111111’
Z = 0

## Slide 73
PIC MCU Instruction Set Literal Operations
ADDLW Add Literal with W
Syntax: ADDLW k
Operands: 0 <= k <= 255
Operation: (W) + k -> (W)
Status: C,DC,Z
Encoding: 11 1110 kkkk kkkk
Words: 1
Cycles: 1
Example:
ADDLW 0x15
Before Instruction
W = 0x10
After Instruction
W = 0x25

## Slide 74
PIC MCU Instruction Set Literal Operations
SUBLW Subtract W from Literal
Syntax: SUBLW k
Operands: 0 <= k <= 255
Operation: k - (W) -> (W)
Status: C,DC,Z
Encoding: 11 1100 kkkk kkkk
Words: 1
Cycles: 1
Example:
SUBLW 0x02
Before Instruction
W = 2
C = ?
Z = ?
After Instruction
W = 0x00
C = 0
Z = 1

## Slide 75
PIC MCU Instruction Set Literal Operations
ANDLW AND Literal with W
Syntax: ANDLW k
Operands: 0 <= k <= 255
Operation: (W) .AND. k -> (W)
Status: Z
Encoding: 11 1001 kkkk kkkk
Words: 1
Cycles: 1
Example:
ANDLW B’01011111’
Before Instruction
W = B’10100011’
After Instruction
W = B’00000011’

## Slide 76
PIC MCU Instruction Set Literal Operations
XORLW Exclusive OR Literal with W
Syntax: XORLW k
Operands: 0 <= k <= 255
Operation: (W) .OR. k -> (W)
Status: Z
Encoding: 11 1010 kkkk kkkk
Words: 1
Cycles: 1
Example:
XORLW B’10101111’
Before Instruction
W = B’10110101’
After Instruction
W = B’00011010’

## Slide 77
PIC MCU Instruction Set Control Operations
k
14-bit Instruction for RETLW
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
SLEEP -
CLRWDT -
RETLW k
RETFIE -
RETURN -
CALL k
GOTO k
Control
Operations
14-bit Instruction for CALL and GOTO
OP CODE
k = 11-bit Immediate Value
k
k
k
k
k
k
k
k
k
k
k

## Slide 78
PIC MCU Instruction Set Control Operations
SLEEP Enter SLEEP mode
Syntax: SLEEP
Operands: None
Operation: 00h -> WDT
1 -> TO
0 -> PD
Status: TO, PD
Encoding: 00 0000 0110 0011
Words: 1
Cycles: 1
Example:
SLEEP

## Slide 79
CLRWDT Clear Watchdog
Syntax: CLRWDT
Operands: None
Operation: 00h -> WDT
0 -> WDT prescaler
1 -> TO
1 -> PD
Status: TO, PD
Encoding: 00 0000 0110 0100
Words: 1
Cycles: 1
PIC Instruction Set Control Operations
Example:
CLRWDT

## Slide 80
PIC MCU Instruction Set Control Operations
RETLW Return with Literal in W
Syntax: RETLW k
Operands: 0 <= k <= 255
Operation: k -> (W)
TOS -> PC
Status: None
Encoding: 11 0100 kkkk kkkk
Words: 1
Cycles: 2
Example:
RETLW 0x5A
After Instruction
W = 0x5A

## Slide 81
PIC MCU Instruction Set Control Operations
RETFIE Return from Interrupt
Syntax: RETFIE
Operands: None
Operation: TOS -> PC
1 -> GIE
Status: None
Encoding: 00 0000 0000 1001
Words: 1
Cycles: 2
Example:
RETFIE

## Slide 82
PIC MCU Instruction Set Control Operations
RETURN Return from Subroutine
Syntax: RETURN
Operands: None
Operation: TOS -> PC
Status: None
Encoding: 00 0000 0000 1000
Words: 1
Cycles: 2
Example:
RETURN

## Slide 83
PIC MCU Instruction Set Control Operations
CALL Call Subroutine
Syntax: CALL k
Operands: 0 <= f <= 2047
Operation: (PC) + 1 -> TOS
k -> PC<10:0>
PCLATH<4:3 -> PC<12:11>
Status: None
Encoding: 10 0kkk kkkk kkkk
Words: 1
Cycles: 2
Example:
Here CALL There
Before Instruction
PC = address Here
After Instruction
PC = address There
TOS = address Here+1

## Slide 84
PIC MCU Instruction Set Control Operations
GOTO Unconditional Branch
Syntax: GOTO k
Operands: 0 <= f <= 2047
Operation: k -> PC<10:0>
PCLATH<4:3> -> PC<12:11>
Status: None
Encoding: 10 1kkk kkkk kkkk
Words: 1
Cycles: 2
Example:
GOTO There
After Instruction
PC = address There

## Slide 85
PIC Instruction Set Byte-Oriented Operations
14-bit Instruction for Byte Oriented Operations
OP CODE
d
f
f
f
f
f
f
f
d = Destination Bit
d = 0 for destination W
d = 1 for destination f
f = 7-bit Register Address
Example:
ADDWF REG, W
ADDWF f, d
NOP -
MOVWF f
CLRW -
CLRF f
SUBWF f,d
DECF f,d
IORWF f,d
ANDWF f,d
XORWF f,d
ADDWF f,d
MOVF f,d
COMF f,d
INCF f,d
DECFSZ f,d
RRF f,d
RLF f,d
SWAPF f,d
INCFSZ f,d
Byte-Oriented
Operations

## Slide 86: 12-bit Core Instruction Set: Byte-Oriented Operations
Byte-Oriented Operation
NOP - No Operation
MOVWF f Move W to f
CLRW - Clear W
CLRF f Clear f
SUBWF f,d Subtract W from f
DECF f,d Decrement f
IORWF f,d Inclusive OR W and f
ANDWF f,d AND W and f
XORWF f,d Exclusive OR W and f
ADDWF f,d Add W and f
MOVF f,d Move f
COMF f,d Complement f
INCF f,d Increment f
DECFSZ f,d Decrement f, skip if zero
RRF f,d Rotate right f
RLF f,d Rotate left f
SWAPF f,d Swap halves f
INCFSZ f,d Increment f, skip if zero
11 6 5 4 0
OPCODE d fffff
d = 0 for destination W
d = 1 for destination f
f = file register address
Notes: Explain the break out of the bits and how it relates to the architecture. I.e. the limited number of bits avail for address effects paging and banking. Also go over the use of the destination bit.

## Slide 87
PIC Instruction Set Bit-Oriented Operations
14-bit Instruction for Bit Oriented Operations
OP CODE
b
f
f
f
f
f
f
f
b = 3-Bit Address
(Bit Number)
f = 7-bit Register Address
b
b
Example:
BTFSC STATUS, C
BTFSC f, b
BCF f,b
BSF f,b
BTFSC f,b
BTFSS f,b
Bit-Oriented
Operations

## Slide 88: 12-bit Core Instruction Set: Bit-Oriented Operations
Bit-Oriented Operation
BCF f,b Bit clear f
BSF f,b Bit set f
BTFSC f,b Bit test f, skip if clear
BTFSS f,b Bit test f, skip if set
11 8 7 5 4 0
OPCODE bbb fffff
f = file register address
b = bit address
Notes: Explain how relates to individual bits addressed.

## Slide 89
PIC Instruction Set Literal and Control Operations
k
14-bit Instruction for Literal Operations
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
Example:
MOVLW 0x2F
MOVLW k
SLEEP -
CLRWDT -
RETLW k
RETFIE -
RETURN -
CALL k
GOTO k
MOVLW k
IORLW k
ADDLW k
SUBLW k
ANDLW k
XORLW k
Literal and Control
Operations

## Slide 90: 12-bit Core Instruction Set: Literal and Control Operations
Literal and Control Operations
OPTION - Load OPTION register
SLEEP - Go into Standby Mode
CLRWDT - Clear Watchdog Timer
TRIS f Tri-state™ Port f
RETLW k Return, place Literal in W
CALL k Call Subroutine
GOTO k Go to address (k is 9 bits)
MOVLW k Move Literal to W
IORLW k Inclusive OR Literal and W
ANDLW k AND Literal W
XORLW k Exclusive OR Literal W
11 8 7 0
OPCODE kkkk kkkk
k = literal value
Note: In GOTO instruction,
literal is 9 bits long
Notes: Explain how literal byte handled in opcode.

## Slide 91: 12-bit Core Instruction Set: Branch Instructions
CALL opcode uses 8-bits for address -> Address for routine must be in 1st 256 locations for each page. PC<8> = 0.
GOTO opcode uses 9-bits for address -> Address any location in a page
PC<10:9> comes from PA1:PA0 (STATUS<6:5>)
0
PC
10
9
8
7
0
Call or Modify PCL Instruction
STATUS<PA1:PA0>
From Instruction OP Code
Bits
PC
10
9
8
7
0
Goto Instruction
STATUS<PA1:PA0>
From Instruction OP Code
Bits
Notes: Remind of connection to architecture and paging/banking.

## Slide 92: 12-bit Core Instruction Set: Example #1
RRF Temp, W
Before Instruction:
Temp = b’10100101’
W = ?
C = 0
After Instruction:
Temp = b’10100101’
W = b’01010010’
C = 1
Note: Contents of Temp did not change

## Slide 93: 12-bit Core Instruction Set: Example #2
Move a value from CONTROL to PORTB
Movf CONTROL,W
Movwf PORTB
Before Instruction 1:
CONTROL = b’10100101’
W = ?
PORTB = ?
Z = ?
C = ?
After Instruction 1:
CONTROL = b’10100101’
W = b’10100101’
PORTB = ?
Z = 0
C = 0
Before Instruction 2:
CONTROL = b’10100101’
W = b’10100101’
PORTB = ?
Z = 0
C = 0
After Instruction 2:
CONTROL = b’10100101’
W = b’10100101’
PORTB = b’10100101’
Z = 0
C = 0
Notes: Ask students what happens anytime a value goes thru the W register?
Status bits get set.

## Slide 94: 12-bit Core Instruction Set: Example #3
DECFSZ Temp, F
GOTO NOTZERO
GOTO ZERO
Note: Contents of Temp does change
What are the instructions DECFSZ and INCFSZ useful for?
NOTZERO
ZERO

## Slide 95: Assembler Directives
LIST
  Syntax: list [<list_option>,…list_option>]
  Ex: list p=16F84A, f=INHX8M, r=DEC
  Description: Select various assembler options
INCLUDE
  Syntax: include “filename.*” or <filename.*>
  Ex: include <p16f84a.inc>
  Description: Assembles the indicated file as if it were in-line code in the source file. Commonly used to create modular code segments.
Notes: Explain assembler directives and why used.
Explain difference between “ “ and < >
< > means file is in default mplab directory

## Slide 96: Assembler Directives
ORG
  Syntax: ORG <address>
  Ex: ORG 0x00
  Description: Start assembling the lines below this statement at location 0x00.
EQU
  Syntax: <label> equ <expr>
  Ex: SECONDS equ 0x24
  Description: Define a text substitution for a constant or variable. Seconds is a constant of 24h or is a register @ address 0x24.
    movlw SECONDS ;const = 24h
    movf SECONDS,W ;value in seconds reg.
Notes: Use data sheets as needed to explain fractured memory (step over interrupt vector, etc. ) and no overrun. Also use data sheets to explain manual address assign vs auto assign from next slide.

## Slide 97: Assembler Directives
CBLOCK
  Syntax: cblock [<expr>]
  Example:
    cblock 0x20 ;Start point of cblock
        hours
        minutes
        seconds
        halfseconds:2
    endc ;Indicates end of cblock
  Description: Declare Symbol Constant

## Slide 98: Assembler Directives (cont)
END
  Syntax: end
  Example: Indicates end of source code.
You must have this statement after the last instruction you want assembled.
Notes: Explain how this directive actually tells the compiler to skip all codes below it.

## Slide 99: Relocatable Code What is it?
Code written to work at any address
In source, code and data are organized into blocks called ‘sections’
The linker assigns sections into memory regions

## Slide 100: Relocatable Code Why use it?
Organization - You can organize your project into multiple files
Reusability - Source files can have a more focused purpose, encouraging code reuse
Faster Development - Recompilation of entire project is not required each time a change is made
Convenience - User does not need to organize and manage individual memory locations

## Slide 101: Relocatable Code In MPASM
CODE - Declares the beginning of a program code section
UDATA - Declares the beginning of an uninitialized data section
BANKSEL - Selects the correct bank for a RAM access
PAGESEL - Selects the correct bank for a ROM access
EXTERN - Indicates a variable that is declared in another module
GLOBAL - Indicates that a variable is referenced in another module

## Slide 102
Devtools

## Slide 103: Unique Tool Support
Project
Manager
Built-in
Editor
Source Level
Debugger
MPASM
Assembler
C Compilers
Languages
Programmers
MPLAB-SIM
Simulator
Simulators
Real-ICE
MPLAB-ICE
2000 & 4000
Emulators/ Debuggers
Third Party
Other tools
MPLINK
MPLIB
SIMICE
Hardware
Simulator
MPLAB
Integrated Development Environment
PICSTART
Plus
PICKIT 2
PRO MATEII
PM 3
MPLAB-ICD2
PICkit 2
Express

## Slide 104: Development Systems MPLAB-ICE
Universal in-circuit emulator for PIC® MCUs
Windows™ compatible
MPLAB compatible
Parallel port interface
Complete source-level debugging
Real-time in-circuit emulation of PIC MCUs
Low voltage emulation
Program memory emulation and memory mapping up to 64K words
Notes: Talk about how not all of these features are on all ice’s.
Talk about how the ice uses processor modules.

## Slide 105: Development Systems MPLAB-ICE (continued)
Break/trace/trigger on program address/data, internal register address/data, external inputs, or bus cycle type (mid-range, hi-end, golden gate only)
Real-time trace with up to 32K x 128 buffer
Time stamp trace
External trigger input and output for logic analyzer/scope interface
Complex breakpoints of up to four levels. Sequential events, AND/OR events, filtered trace, time between two events, and pass counts.

## Slide 106: MPLAB-ICE 2000
Host to Pod Cable
*Emulator Pod
*Processor
Module
Flex Circuit
Cable
*Device
Adapter
*SOIC
Transition
Socket
*Each component
ordered separately

## Slide 107: Development Systems ICEPIC
Low cost in-circuit emulator for PIC MCUs
Developed by RF Solutions (U.K.)
Windows-compatible
Complete source-level debugging
EIA232 serial interface
Unlimited breakpoints

## Slide 108: Development Systems MPLAB-SIM
Universal simulator for PIC MCUs
Windows and MPLAB-compatible
Discrete event instruction-based simulation
Complete source-level debugging
Support interrupts and most peripheral functions (not A/D or serial I/O)
Stimulus injection and file input capability
Free

## Slide 109: Development Systems MPLAB-ICD 2
Features
      USB (Full Speed 2 M bits/s) & RS-232 interface to host PC
      Real time background debugging
      MPLAB IDE GUI (free copy included)
      Built in over-voltage/short circuit monitor
      Firmware upgradeable from PC
      Totally enclosed
      Supports low voltage to 2.0 volts. (2.0 to 6.0 range)

## Slide 110: Development Systems MPLAB-ICD 2
Features Continued
      Diagnostic LEDs (Power, Busy, Error)
      Reading/Writing memory space and EEDATA areas of target microcontroller
      Programs configuration bits
      Erase of program memory space with verification
      Peripheral freeze-on-halt stops timers at breakpoints

## Slide 111: Development Systems MPLAB-ICD 2
There is some shared overhead expense that includes:
      one stack level,
      some general purpose file registers
      a small area of program memory when in the debug mode

## Slide 112: Development Systems PICSTART Plus
Development programmer kit
Supports all PIC MCUs
Windows- and MPLAB-compatible
CD-ROM literature

## Slide 113: Development Systems PICSTART Plus Development Programmer
Upgrades done in MPLAB software - firmware upgrades occasionally required for new PIC sub-families
Uses serial programming algorithms for all ICSP capable devices
PICSTART Plus
DEVELOPMENT PROGRAMMER
POWER
ACTIVE
RS-232 Serial
Interface
9V DC Input
Power ON
Programmer
Active
40-Pin ZIF Socket to accommodate PICs from 8- to 40-pins. 68-pin PLCC can be programmed with an adapter
Pin-1

## Slide 114: Development Systems PRO MATE® II
Universal device programmer for PIC MCUs
Stand-alone or PC DOS-compatible, MPLAB-compatible
EIA232 PC host interface
Interchangeable socket modules
Environment “save and restore”
Programmable voltages for verify
Serialized programming capabilities
ICSP support
Serial EEPROM support
KEELOQ® support

## Slide 115: Development Systems PICDEM-1, -2, -3, -14, -17
Demonstration board for PIC MCUs
On board +5V regulator
EIA232 interface
5K pot to simulate analog input
3 push buttons for external stimulus and reset
LED’s connected to PORTB
LCD display panel connection
Socket for crystal oscillator
Prototype area
Notes: -1 => 18 pin max
-2 => 40 pin max

## Slide 116
Development Systems PICDEM-1 Demo Board
Demo board
accommodates all 18-pin
PIC devices, 28-pin
PIC16C5X and 40-pin
PIC17C4X devices
8-LEDs connected to
PORTB
5k Pot connected to AN0
PB switches connected
to RA1, RTCC, and MCLR
LED
RS-232
Serial Interface
Crystal Oscillator
Socket
9V DC Input
Prototyping
Area
Potentiometer
on A/D Channel 0
RTCC
MCLR
RA1
RS-232 Level
Shifter (MAX-232)

## Slide 117: Development Systems MPASM
Universal macro assembler for all PIC MCUs
DOS- and Windows-compatible
Compatible with MPLAB
  Symbolic and source-level debugging
  Can generate relocatable code
Multiple output formats
Licensed by several third party vendors
Free

## Slide 118: Development Systems COMPILERS
Microchip MPLAB-C17
Microchip MPLAB-C18
Microchip MPLAB-C30
Hi-Tech
CCS
IAR
Byte Craft
Micro Engineering Labs (Basic)

## Slide 119: Development Systems Reference Materials
Application notes
  Embedded Controls Handbook
Reference designs
Website
  http://www.microchip.com
  Conference groups
  Mailing lists
Microchip CD ROM
Template subdirectory under MPLAB (code templates)
Seminars
Workshops

## Slide 120: Development Systems Third Party Guide
Microchip encourages third-party support
  312-page reference manual to aid in selection of appropriate tools
  106 companies and 208 products
    Emulators
    Programmers and gang programmers
    ‘C’ compilers, software, demo boards, etc.
  Design consultant reference

## Slide 121: Books For Further Research (English)
Design with PIC Microcontrollers, John Peatman, Prentice-Hall, 0-13-759259-0
Programming and Customizing the PIC Microcontroller, Myke Predko, McGraw-Hill, 0-07-913646-X
Easy PIC’n, David Benson, Square 1 Electronics, 0-9654162-0-8
PIC’n Up The Pace, David Benson, Square 1 Electronics, 0-9654162-1-6
A Beginners Guide to the Microchip PIC, Nigel Gardner, Bluebird Technical Press Ltd., 1-899013-01-6

## Slide 122: Books For Further Research (English)
PIC Cookbook Vol 1 & Vol 2, Nigel Gardner, Bluebird Technical Press Ltd., 1899013-02-4, 1-901631-00-1
The Greatest Little PIC Book, Gordon McNee, Bluebird Technical Press Ltd., 1-901631-01-X
PIC Microcontroller Operation and Applications, DN de Beer, Cape Technikon, daandb@norton.ctech.az.za
Getting started with PIC Microcontrollers, Al Stevens, Ziggurat Technologies, ziggurat@global.co.za

## Slide 123: Books For Further Research (French)
Les Microcontrolleurs PIC et mise en oeuvre, Christian Tavernier, Dunod, 2-10-002647-X
Micontrolleurs PIC a structure RISC, C.F. Urbain, Publitronic, 2-86661-058-X
Pratique des Microcontroleurs PIC, Francesco Volpe/Safinaz Volpe, Publitronic Elektor, 2-86661-077-6

## Slide 124: Books For Further Research (German)
Mit dem PIC-Controller Erfolgreich Arbeiten, Dr. Anne Koenig/Manfred Koenig, Markt & Technik Verlag, 3-8272-5168-0
Mikrokontroller mit RISC Struktur, C.F. Urbain, Elektor Compact, 3-928051-83-0
Mikroprozessor PIC16C5X, Michael Rose, Huthig, 3-7785-2169-1
Mikroprozessor PIC17C42, Michael Rose, Huthig, 3-7785-2170-5
PIC uC Praxis, Francesco Volpe/Safinaz Volpe, Elektor Verlag, 3-89576-030-7

## Slide 125: Books For Further Research (Italian/Russian/Spanish)
La Programmazione dei Microcontrollori PIC, Andrea Sbrana, Italy +39 544 464070
New Possibilities with the Microchip PIC, RIGA, Latvia +371 935 0550
MicroControladores PIC La Solution en un Chip, Martinez Usategui, Paraninfo,84-283-2371-2
MicroControladores PIC, Christian Tavernier, Paraninfo, 84-283-2373-9

## Slide 126: Books For Further Research (Chinese)
Parts 1-5 PIC16C5X/71/84 Development and Design, United Tech Electronic Co. Ltd,
  957-21-0807-7
  957-21-1152-3
  957-21-1187-6
  957-21-1251-1
  957-21-1257-0
PIC16C84 MCU Architecture and Software Development, ICC Company, 957-8716-79-6

## Slide 127: Microchip Technical Services Engineering Web Site
Web address: www.microchip.com
Latest versions available
  Datasheets
  User’s Guides
  Application Notes
  Device Errata
  Development tools
Frequently-Asked Questions (FAQs)
Latest product announcements
Recent press releases

## Slide 128: Microchip Technical Services
Workshops
  Hands on workshops using Microchip development tools
  Various topics in many cities
  Watch the web site for details
Address: www.microchip.com

## Slide 129: On to the Labs

## Slide 130: Lab 1 PIC12C672 14-bit core
Notes: In each of the steps following for lab 1, have the students watch first then do the actions of their machines.

## Slide 131: Lab1
Objective:
Program an OTP and plug it into your PIC & Stick take home demo board
  1st time experience with tools
  Will use PIC & Stick board with non-coded PIC’s
Notes: Teach students how to setup a project file, build project, program part. General tools usage. Use picNstick with the non-coded pics. Go thru a review of what each of the buttons are and do. Especially when using the simulator.

## Slide 132: Lab 1 MPLAB Layout
Development Mode
Target Processor
Run
Halt
Step
Reset
Make

## Slide 133: Lab 1 Selecting Hardware Options
Use Debugger > Select Tool > MPLAB SIM… to select execution environment
Use Configure > Select Device to select processor
Use Debugger > Settings > Clock TAB to select oscillator frequency
  MPLAB-ICE uses a programmable clock
  MPLAB-SIM only uses frequency for time calculations

## Slide 134: Lab 1 MPLAB Projects
MPLAB projects manage:
  Installed build tools
  Development mode
  Hardware settings
  Source files
  Dependencies (*.inc, *.h)
  Compile, link, and assembly options

## Slide 135: Lab 1 Creating a New Project
Choose Project > New Project… from the menu, and select a filename for your project

## Slide 136: Lab 1 Setting Build Options

## Slide 137: Lab 1 Configuring Build Tools
Microchip’s tools are configured for use during installation
For other tools, use Project > Select Language Tool Suite...
Use the Active Toolsuite: pulldown bar for other Language toolsuites

## Slide 138: Lab 1 Using the Project Window
Quick access to project summary
  Source files
  Dependencies

## Slide 139: Setting Up MPLAB IDE Projects Program Your Part
Verify that your program is listed in the “Program Memory Window”
If it is not, build your project again to update the “Program Memory Window”
Verify device settings in the PICSTART Plus Device Programmer window
Insert part to be programmed with correct pin 1 orientation
Click on Program to program part

## Slide 140: Lab notes
Must make a project first, prior to programming part
Make sure that the .asm file is listed in the project as a file to be built
Must build the .asm file to create a .hex file prior to programming part
Make sure that correct part is selected on programmer
Must set configuration bits for the operating mode of the part

## Slide 141: What feature set (reminder)
  Open/close
  Switch controlled
  Held open to allow passage thru door
  Automatic close (store type)
  Safety cutoffs (if time permits)
  Independent motor control (if time permits)
  Double tap (if time permits)
  Lighting control (optional)
  Sound control* (optional)
Notes: Note to students that from lab 2 on, all of the work they do is heading towards the final project so review the final project specs. Mention/elicit from students what aspects, switching, timing, etc are uesd to achieve each of the project specs.

## Slide 142: Lab 2 Using An I/O Port (Switching) PIC12F508 12-bit Core

## Slide 143: Lab notes: Peripheral Used: Digital I/O Ports
6 - 20 I/O pins
Each I/O pin software configurable as input or output
Direct bit manipulation (single-word/single-cycle):
Bit set
Bit clear
High drive capability
  25mA sink max (all parts)
  60mA sink max (PIC17CXXX)
  25mA source max
Can directly drive LEDs:
Notes: <number>
<footer>
<header>
<date/time>
On reset I/O are defaulted to High Impedance inputs
NOTE: Each pin has a high drive capability, but Ports also have current maximums (due to Vdd/Vss electromigration issues - device reliability issue).

## Slide 144: Peripherals: Digital I/O Port (Cont.)
Data Bus
Wrt. Port
D
Q
Q
SET
CLR
D
Q
Q
SET
CLR
W Reg
Tris f
Rd. Port
I/O Pin
Data Latch
Tris Latch
Vss
Vdd
Reset
Notes: <number>
<footer>
<header>
<date/time>
I/O pin structure
When pin is in Reset start, the pin is a high impedance input (both transistors are turned off)

## Slide 145: Lab Notes: Read-Modify-Write
PC
PC + 1
PC + 2
PC + 3
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Instruction
fetched
RB7:RB0
MOVWF PORTB
write to
PORTB
NOP
Port pin
sampled here
NOP
MOVF PORTB,W
Instruction
executed
MOVWF PORTB
write to
PORTB
NOP
MOVF PORTB,W
PC
TPD
Note:
This example shows a write to PORTB
followed by a read from PORTB.
Note that:
data setup time = (0. 25TCY-TPD )
where
TCY= instruction cycle
TPD = propagation delay
Therefore, at higher clock frequencies,
a write followed by a read may be problematic.
Consider loads on pins for back to back read-modify-writes
Qcy = Fosc
Instruction cycle = Fosc/4
Notes: Explain read modify write. Use example of stray capacitance on a pin being written to then read with no nop in between and how the rc curve effects the read back value.

## Slide 146: Workshop Board Schematic (excerpt)

## Slide 147: Lab2 Using An I/O Port
Objective:
Drive port pin GP4 to a logic 1
Verify code with the MPLAB Simulator
Program a part and test it in your workshop board
Notes: All labs from lab2 on out are to develop modules. The latter labs will have the students combining the modules to handle base functions and adding features modules as each new set of functions are added.

## Slide 148: Make a project file review

## Slide 149: Setting Up MPLAB IDE Projects Make A .asm File
File -> New
  This opens a text window where you can begin entering your code
Type in program header
File -> Save As
  Save the file as lab2.asm
File -> Close

## Slide 150: Setting Up MPLAB IDE Projects Make A Project File
Project -> New
  Type Lab2 in Project Name Box
  Click Browse: Find Folder: C:\PIC101 Click the Select button
    Click on OK
  Project Files
    Right Click on Source files
      Select Add Files
      Find Lab2.asm Click Open
Notes: This review is in as needed. Is recommended to have them watch instructor as he runs thru making a project but with lab2 file names. Then have the students do it. Is a good reminder.

## Slide 151: Setting Up MPLAB IDE Projects Make A Project File (cont.)
  Project Files Continued
    Right Click on Header files
      Select Add Files
      Find c:\Program Files\MPLAB IDE\MCHIP_tools\P12C508A.inc
      Click Open
Notes: This review is in as needed. Is recommended to have them watch instructor as he runs thru making a project but with lab2 file names. Then have the students do it. Is a good reminder.

## Slide 152: Setting Up MPLAB IDE Projects Make A Project File (cont.)
  Project Files cont.
    Debugger > Select Tool > MPLAB SIM
    Configure > Select Device
      Use Device: pull down Bar
        Select the appropriate part [12C508A]
        Click on OK (Close Select Device Dialogue box)

## Slide 153: Setting Up MPLAB IDE Projects Verify Correct .asm File
Verify that the “Node: lab2.asm” file is the correct file you are working on.
Double click on lab2.asm in the Lab2.mcw Project window
  Lab2.asm will be used for this project

## Slide 154: Code Ex2 - Light an LED
  ;**********************************************************************
  ;This program drives a 1 onto port pin GP4
  ;**********************************************************************
  List P=12F508, R=hex
  include <P12F508.inc> ;load the include file
  __CONFIG _IntRC_OSC & _WDT_OFF & _CP_OFF & _MCLRE_ON
org 0x00 ;indicate the start location
Start clrf GPIO ;load output latch w/zeros
movlw 0x00 ;Configure port to outputs
tris GPIO ;
bsf GPIO,4 ;set pin 4 on GPIO (GP4) to logic 1
Loop nop
goto Loop ;$ = current address... infinite loop
end
Notes: This is where I have the students fire up MPLAB and I walk them through setting up a project and creating a file with the above code. Finish all of the slides including the review of the simulator’s controls before having them type in the above code. We will go back to this slide after the sim review.
Go over the above code to illustrate the minimum requirements of an assembly file.
Use MPLAB-SIM’s watch windows to illustrate the how the above code executes the part.

## Slide 155: Create a Watch Window
View -> Special Function Registers
View -> Watch -> New Watch Window
  Use pull down menu to select registers/variables to watch
  Click Add FSR button after each one or Click Add Symbol button
Notes: Show how to view bin vs hex

## Slide 156: Use simulator to step thru the code
Debugger -> Run
  F6 Reset
  F7 Step
  F8 Step Over
  F9 Run
  F5 Halt
  Ctrl + F9 Animate
Notes: Review simulator buttons and other general controls.

## Slide 157: Lab notes
Must declare org statements so assembler knows code/memory organization
Don’t forget to declare variables if needed
Must configure port pins prior to writing to them

## Slide 158: Lab3 Timing PIC12F508 12-bit Core

## Slide 159: Lab notes: Peripheral Used: TMR0
Readable and writable
Generates interrupt on overflow from FFh to 00h
Prescaler is programmable
In timer mode: fastest increment rate is OSC/4 (5 MHz @ 20 MHz oscillator frequency)
In counter mode: configurable to increment on either edge
External counter mode has Max. input = 50 MHz (using prescaler)
Writing to TMR0 causes an error of 2 Tcy
Ext clock
input
Internal clock
8-bit prescaler
8-bit timer/counter
Interrupt on overflow (not on PIC12C508A)
Notes: <number>
<footer>
<header>
<date/time>
A write to TMR0, automatically clears the prescaler. After a write to the TMR0, there is a 2 cycle delay before a actual increment occurs, this has to be taken into account for accurate time measurements.
The prescaler is asynchronous. The input clock to the TMR0 register is synchronized after the prescaler
So if an external clock source is selected, higher clock frequencies then the device frequency can be used (frequency depends on prescaler value).
The value of the prescaler is not readable

## Slide 160: Lab Notes:
Timing Loop
Counting Loop
Nested Loop
Branch Control
BTFSS
BTFSC
DECFSZ
INCFSZ
Notes: Explain how timing/counting/nested loops work. Why they are good for quick and dirty timing but how they tie up processor and burn up cycles which could have been used for something else.

## Slide 161
OPTION REG
PIC12F508
W-1
W-1
W-1
W-1
W-1
W-1
W-1
W-1
GPWU
GPPU
T0CS
T0SE
PSA
PS2
PS1
PS0
W= Writable bit
U= Unimplemented bit
- n= Value at POR reset
Reference Table4-1 for other
resets.
bit7
6
5
4
3
2
1
bit0
bit
5:
T0CS
: Timer0 clock source select bit
1 = Transition on T0CKI pin
0 = Transition on internal instruction cycle clock, Fosc/4
bit
4:
T0SE
: Timer0 source edge select bit
1 = Increment on high to low transition on the T0CKI pin
0 = Increment on low to high transition on the T0CKI pin
bit
3:
PSA
: Prescaler assignment bit
1 = Prescaler assigned to the WDT
0 = Prescaler assigned to Timer0
bit
2-0:
PS2:PS0
: Prescaler rate select bits
000
001
010
011
100
101
110
111
1
:
2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
1 : 256
1 : 1
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
Bit Value
T
imer0
Rate
WDT Rate
Notes: Review control bits in option register. Explain how on 12bit cores the option is a command but on 14bit core it is a register. (option_reg) use data sheets to show difference. Will remind them of diference in latter lab.
Cover other items like woc, pullups, etc.

## Slide 162: Lab3 Timing
Objective
Write an approx. 2 ms delay loop program using TMR0
  Typically used to
    provide timing for delaying/controlling events
    provide timing for tracking events
Do not use the prescaler
Pre-load TMR0 to count 200 micro seconds
Light 2 LEDs to indicate status
  GP4 LED2 should light to indicate that your program is running
  GP5 LED1 should light when the approx. 2 ms delay has occurred
Verify using MPLAB simulator with stopwatch
Notes: Use tmr0 module and also highlight how this can be done w/ no interrupts (12bit core). Go thru timing calculations with class.

## Slide 163: Lab notes: Calculate # of TMR0 Roll Overs
Part uses a 4Mhz clock
TMR0 clocks @ a rate of Fosc/4
  if prescaler not used
TMR0 rolls over from FFh to 00h
How many counts does a s/w counter need to get approx. 2 ms?
How many counts does a s/w counter need to get approx. 2 ms if tmr0 only counts 200 micro seconds?

## Slide 164: Code Ex3 - 2 ms delay
;***************************************************************
;approx. 2 ms delay program with 2 status leds to show start and end of delay
;***************************************************************
  List P=12F508, R=hex
  include “P12F508.inc” ;load the include file
  __CONFIG _IntRC_OSC & _WDT_OFF & _CP_OFF & _MCLRE_ON
  cblock 0x07
  COUNTER
  endc
  Org 0x00
  movwf OSCCAL ;setup INTRC calibration
  .
  .
  Place your code here
  .
  .
  end
Notes: Have them use the lab3 template already created.

## Slide 165: Code Ex3 - 2 ms delay (cont.)
Set Prescaler
Light 1st LED
Reset TMR0
2
ms?
Light 2nd LED
Notes: Review how flow chart breaks down the problem into manageable pieces.

## Slide 166: Lab notes
  The PIC12F508 has an 8 bit timer (TMR0) with a selectable prescaler (up to 8 bits)
  You may need to pre-load TMR0 to get the desired time
Notes: The purpose of this exercise is to illustrate how additional hardware peripherals can off-load the processor so that it is available to handle multiple tasks at the same time.
Start by explaining the concept of interrupts and that we use them to allow hardware peripherals to perform fixed tasks without loading the processor’s core.
Explain the TMR0 peripheral and how we could use it to count instruction cycles while we do something else in the main routine. It may take a while to explain the prescaler’s function and how to set it up.
Explain the GIE and T0IE. Explain how the T0IF bit works.
Write the code.

## Slide 167: Lab notes: Sample window
What happens if the FFh -> 00h roll over occurs after you have sampled?
Use a Sample Window
Notes: Explain how since no interrupts how to handle tmro roll over events before letting students start writing code. Will go back to template slide if needed.
Before release students to write code, have them setup processor options. INTRC, stack overflow, etc.

## Slide 168: Lab3 Timing
Review sample code lab3.asm provided by the instructor.
Notes: Give them 20-30 min to attack the problem then review the insturctors lab3.asm explaining why things were done the way they were. Be sure and review sample window. Show how to use stop watch to verify time.

## Slide 169: Lab4 Timing PIC16F84A 14-bit Core
Notes: Lab 4 introduces interrupts. Has students do same thing as lab3 but with interrupts.

## Slide 170: Feature Used: Interrupts
RBIF
RBIE
T0IF
T0IE
INTF
INTE
GIE
EEIE
Wake
-
up
(If in SLEEP mode)
Interrupt to CPU
EEIF

## Slide 171
INTCON REG
PIC16F84A
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-x
GIE
EEIE
T0IE
INTE
RBIE
T0IF
INTF
RBIF
R= Readable bit W= Writable bit
U= Unimplemented bit, read as ‘0’
- n= Value at POR reset
bit7
bit0
bit 7:
GIE:
Global Interrupt Enable bit
1 = Enables all un-masked interrupts
0 = Disables all interrupts
bit 5:
T0IE
: TMR0 Overflow Interrupt Enable bit
1 = Enables the TMR0 interrupt
0 = Disables the TMR0 interrupt
bit 2:
T0IF
: TMR0 Overflow Interrupt Flag bit
1 = TMR0 has overflowed (must be cleared in software)
0 = TMR0 did not overflow
Notes: Review intcon bits.

## Slide 172
OPTION REG
PIC16F84A
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
RBPU
INTEDG
T0CS
T0SE
PSA
PS2
PS1
PS0
R= Readable bit W= Writable bit
U= Unimplemented bit, read as ‘0’
- n= Value at POR reset
bit7
bit0
bit
5:
T0CS
: TMR0 Clock Source Select bit
1 = Transition on RA4/T0CKI pin
0 = Internal instruction cycle clock (CLKOUT)
bit
4:
T0SE
: TMR0 Source Edge Select bit
1 = Increment on high-to-low transition on RA4/T0CKI pin
0 = Increment on low-to-high transition on RA4/T0CKI pin
bit
3:
PSA
: Prescaler Assignment bit
1 = Prescaler assigned to the WDT
0 = Prescaler assigned to TMR0
bit
2-0:
PS2:PS0
: Prescaler Rate Select bits
000
001
010
011
100
101
110
111
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
1 : 256
1 : 1
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
Bit Value
TMR0 Rate
WDT Rate
Notes: Review option bits.

## Slide 173: Workshop Board Schematic (excerpt)

## Slide 174: Why Interrupts
Better use of CPU resource
Faster response time
Multi-tasking
Fixed or known interval handler
Exception handler

## Slide 175: Lab notes: Interrupt Service Routines; Context Changes
Push macro
movwf W_TEMP ;push W and STATUS
swapf STATUS,W ;
movwf STATUS_TEMP ;
endm
Pop macro
swapf STATUS_TEMP,W ;pop W and STATUS
movwf STATUS ;
swapf W_TEMP,F ;
swapf W_TEMP,W ;
endm
Notes: Explain context changes. Have students answer why important.

## Slide 176: Lab4 Timing
Objective
Write an approx. 2 second delay loop program using TMR0 and interrupts
  typically used to
    provide timing for delaying/controlling events
    provide timing for tracking events
Use prescaler
Light 2 LEDs to indicate status
  RB2 LED1 should light to indicate that your program is running
  RB3 LED2 should light when the approx. 2 sec delay has occurred
Verify using MPLAB simulator and on your workshop board when finished
Notes: Use tmr0 module and also highlight usage of interrupts. Go thru timing calculations with class.

## Slide 177: Lab notes: Calculate # of TMR0 Roll Overs
Part uses a 4Mhz clock
TMR0 clocks @ a rate of Fosc/4
  if prescaler not used
TMR0 rolls over from FFh to 00h
Prescaler set to max
How many counts does a s/w counter need to get approx. 2 sec.?

## Slide 178: Code Ex4 - 2 sec delay
;***************************************************************
;approx 2 sec delay program using interrupts with 2 status leds to show start and end of delay
;***************************************************************
  List P=16F84A, R=hex
  include “p16f84a.inc” ;load the include file
  __CONFIG _XT_OSC & _WDT_OFF & _CP_OFF & _PWRTE_ON
  cblock 0x0C
  COUNTER
  W_TEMP
  STATUS_TEMP
  endc
  Org 0x00
  goto Start
  Org 0x04
  goto Int_serv_routine
Notes: This template provided. Just review structures. Students do need to type this in.

## Slide 179: Code Ex4 - 2 sec delay
  Org 0x05
  Start
  .
  .
  Place your code here
  .
  .
  Int_serv_routine
  .
  .
  Place your code here
  .
  .
  end

## Slide 180: Code Ex4 - 2 sec delay (cont.)
Set Prescaler
Light 1st led
Reset TMR0
Wait for
Interrupt
Light 2nd led
Setup Interrupts
What
caused Int
ISR
2
sec?
Notes: Review flow chart again. Re-explain how this helps.

## Slide 181: Lab notes
  The 16F84A has an 8 bit timer (TMR0) with a selectable prescaler (up to 8 bits)
  You may need to pre-load TMR0 to get the desired time
  The main program should be an endless loop (goto $)
  The interrupt vector is address 0x04
  Assert RB3 in the Interrupt Service Routine as status indicator
  Keep ISR as simple as possible. Fill with calls as needed.
Notes: The purpose of this exercise is to illustrate how additional hardware peripherals can off-load the processor so that it is available to handle multiple tasks at the same time. Explain goto $ and how it helps.
Start by explaining the concept of interrupts and that we use them to allow hardware peripherals to perform fixed tasks without loading the processor’s core.
Explain the TMR0 peripheral and how we could use it to count instruction cycles while we do something else in the main routine. It may take a while to explain the prescaler’s function and how to set it up.
Explain the GIE and T0IE. Explain how the T0IF bit works.
Write the code.

## Slide 182: Lab4 Timing
Review sample code lab4.asm provided by the instructor.
Notes: Give students about 20-30 minutes to hack at this one. Then review the instructors lab4 code.

## Slide 183: Lab5 Motor Control PIC16F84A 14-bit Core

## Slide 184: Motor Connection Schematic

## Slide 185: Lab5 apply to simple motor control
Objective
Apply labs 2 and 4 to control door motors
Motor control to drive doors both open and close
Toggle opening and closing of door in a repeating cycle
Validate using MPLAB simulator, your workshop board, and the scale model prototype when finished
Notes: Students need to beware that there are 2 motors that they need to drive simultaneously. Porta is wired to the 2 motors with pins <1:0> tied to motor left and pins <3:2> tied to motor right.
Students should use workshop board for this lab. Explain features of the workshop board here.
Students should use scale prototype board from labs 6 on as tests of their burned code.
*Note to class
Can be more efficient and design to control motors w/ just 1 pin by using H-bridge but for purposes of class, use 2 pins.

## Slide 186: Lab notes
Motor biasing is set for standard logic
2 control bits are required for each motor
You will need to stop the motion of the motor before reversing it’s direction to avoid stripping motor’s gears
Use the timing and I/O port control modules you developed earlier to help you
PORTA is tied to the 2 door motors
Notes: Must stop motor’s motion to avoid stripping the motors gears.
Note to students that when using the workshop board, only port A is wired to the leds via the c57 part.

## Slide 187: Lab 6 Sensing an Input PIC16F84A 14-bit Core

## Slide 188: Lab6 add sensing/inputs (2 part lab)
Mechanical catch/releases vs electrical switches
Floor pad/wall switch
Input techniques
  polling
  external interrupt on INT pin
  interrupt/wake up on change
Notes: Spend some time going over the different input techniques and advantages and limitations of each. Use following slide as needed.

## Slide 189: Input techniques
Polling
  sample window roll over
  power consumed
  ringing input
  debouncing of input signal
External interrupt on INT pin
  multiple interrupts
  sequential servicing
  simultaneous interrupts
Interrupt/wake up on change
  can put part to sleep prior to receiving interrupt input
  battery type apps

## Slide 190: Lab 6 (a) Polling Input Pin

## Slide 191: Why Debounce?
Ringing inputs
Noisy inputs
Glitch on input

## Slide 192: Debounce push button/key Ringing or noisy inputs
AN 566 contains debounce
Check_key
;poll for key press
btfsc PORTB,1 ;
goto Check_key ;
; call Debounce_delay ;debounce signal
btfsc PORTB,1 ;check for bouncing input
goto Check_key ;
return
;routine to give delay for key bounce routine
Debounce_delay
.
.
delay routine here
.
return
Notes: Use this code to explain how to handle signal bounce.

## Slide 193: Polling Input Schematic

## Slide 194: Lab 6 (a) of 2-step lab
Objective
Read input by polling, (foot pad) to activate door “opening/closing sequence” module you developed earlier
Momentary switch on port pin RB1
RB1 is an active low input
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished

## Slide 195: Code Ex6a - Polling Input
Set Prescaler
Reset TMR0
Wait for
Interrupt
Setup Interrupts
RB1
Lo?
Door Control
State Machine
What
caused Int
ISR
2
sec?
Notes: Review flow chart.

## Slide 196: Lab notes
Call a input checking routine from your main loop
Might need a state machine to track the different phases (open, close, etc.) and coordinate with your timing routines
Must loop back to look for next input

## Slide 197: Lab 6 (b) Interrupt on INT Pin

## Slide 198: Feature Used: Interrupt on INT Pin PIC16F84A
RBPU
(1)
I/O
pin(2)
Data Latch
P
VDD
Q
D
CK
Q
D
Q
D
EN
Data bus
WR Port
WR TRIS
RD TRIS
RD Port
Weak
pull-up
RD Port
RB0/INT
TTL
Input
Buffer
Schmitt Trigger
Buffer
TRIS Latch
Note 1: TRISB = '1’ enables weak pull-up
(if RBPU = '0' in the OPTION_REG register).
2: I/O pins have diode protection to VDD and VSS.
CK

## Slide 199: INT Pin Schematic

## Slide 200: Lab6 (b) of 2 step lab
Objective
Read input by interrupt on INT pin (optical sensor) to activate door opening/closing module you developed earlier
Light sensor on port pin RB0
RB0 is active low sensor input
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished
Notes: Want to teach them int on int pin.

## Slide 201: Code Ex6b - INT Pin Input
Set Prescaler
Reset TMR0
Sleep or
Wait for
Interrupt
Setup Interrupts
Int on INT pin
Door Control
State Machine
What
caused Int
ISR
2
sec?
TMR0
Notes: Review flow chart.

## Slide 202: Lab notes
Use different setup routines for the different interrupt modes
Might need a state machine to track the different phases (open, close, etc.) and coordinate with your timing routines
Don’t forget to put part to sleep or in a dead loop while waiting for interrupt on INT pin input (don’t overrun into unwanted areas)
Must loop back to look for next input
Notes: They need to control when T0IE and RBIE modes are active.

## Slide 203: Lab7 State Logic/Higher Order Functions PIC16F84A 14-bit Core

## Slide 204
RBPU
(1)
Data Latch
P
VDD
Q
D
CK
Q
D
CK
Q
D
EN
Q
D
EN
Data bus
WR Port
WR TRIS
Set RBIF
TRIS Latch
RD TRIS
RD Port
From other
RB7:RB4 pins
weak
pull-up
RD Port
Latch
TTL
Input
Buffer
I/O
Feature Used: Interrupt On Change PIC16F84A
Note 1: TRISB = '1’ enables weak pull-up
(if RBPU = '0' in the OPTION_REG register).
2: I/O pins have diode protection to VDD and VSS.

## Slide 205: Peripheral Used PortB Interrupt on Change example
Internal pull-ups (software option) keep RB4-RB7 pins high
RB0-RB3 pins drive '0's
Any key pressed pulls down an RB pin and generates an interrupt
This interrupt wakes up processor from SLEEP
Saves timer resources
Keypad interface:
PIC16CXXX
RB0
RB1
RB3
RB4
RB5
RB6
RB7
RB2
Hex keypad
R †
† Resistance for ESD protection
100 
AN557
Notes: <number>
<footer>
<header>
<date/time>
This example shows how the internal pull-up resistors on RB7-RB4 can be used in conjuction with the change of PortB interrupt to wake the device from sleep when a key is hit.

## Slide 206: Interrupt On Change Schematic

## Slide 207: Lab7 State logic/higher order functions
Objective
Delay to hold door open approx 2 seconds before auto closing
Use “interrupt on INT pin” input method from Lab6(b) to start door sequence
Option 1
  Motor cutoffs
    Position feed back
    Use interrupt on change
Notes: Emergency cut offs are momentary switches tied to the INT on change pins of the pic (RB7:RB4). Explain why might want independent morot controls. Show how this works on workshop board and on scale prototype.
Instructors lab 8 only implements 2 sec delay to hold doors open to let people to walk thru. Instructors lab9b shows full functionality with position feedback, independent motor control, and 2 sec safety hold of door if someone in the way.

## Slide 208: Lab7 State logic/higher order functions
Objective (cont.)
Option 2
  Do not close doors if INT pin sensor still active
  Safety feature
  People still in the doorway
Option 3
  Independent motor cutoff
  Different motor speeds
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished

## Slide 209: Lab notes
Might need a state machine to track the different phases (open, hold open, close, etc.) and coordinate with your timing routines
Use different setup routines for the different interrupt modes
If adding motor cutoffs (option1), don’t use timing delay module while motors running (open or close). But use timing delay to hold door open for 2 sec.
Safety check (option2) only applies when closing doors

## Slide 210: Lab8 Proof Final Functionality PIC16F84A 14-bit Core

## Slide 211: Lab8 combine labs 6 & 7
Objective
Demonstrate final functionality of automatic door controller on workshop prototype board
  Combine all of the developed modules
  Demonstrate optional features if developed (I.e. emergency cutoffs, access light, double tap logic)

## Slide 212: If time permits, discuss a hypothetical design (I.e. home heating/cooling controller) from start to finish

## Slide 213: MCU Robust Design Techniques

## Slide 214: Robust Design Techniques Watchdog Hardware
Helps recover from software malfunction
Uses its own free-running on-chip RC oscillator
WDT cannot be disabled by software
WDT overflow resets the chip
CLRWDT instruction clears WDT
Programmable time-out period: 18 ms to 2.5 seconds
Operates in SLEEP
On time-out wakes up CPU
8-bit ripple counter
"CLRWDT"
Reset
Overflow
resets
chip
Postscaler
RC
oscillator
Notes: <number>
<footer>
<header>
<date/time>
The WDT and TMR0 share the same 8 bit pre-scaler.
A WDT time-out from SLEEP will not cause a reset, but continuation of the program at the next instruction after sleep.
Note: most of the issues with re-assignment of the pre-scaler have been covered in the TMR0 section.

## Slide 215: Robust Design Techniques Watchdog Software Strategies
Watchdog effectivness is only as good as the software controlling it
Use one CLRWDT instruction for the entire program
Place CLRWDT in the main loop
Do not place CLRWDT in ISR or any sub-routines
Select the minimum WDT timeout period that main loop timing can tolerate
Initialize unused memory as GOTO wdtreset (self-loop) to force timeout

## Slide 216: Robust Design Techniques Robust Software - Filling Unused Memory
When using watchdogs, fill unused memory locations with a GOTO wdtreset
This self loop is normally never executed
If the PC is corrupted, it is likely it will execute this instruction
  Force a WDT reset to re-initialize the core
FILL can be used to insert these instructions (Substitute <last location+1> for 400h):
FILL (GOTO wdtreset), (400h-$)
ORG 3FFh

## Slide 217: Robust Design Techniques Robust Software - Clean WDT reset
To force WDT reset on power-up:
  Check for RAM pattern at power-up
  If pattern is not there:
    Initialize RAM pattern
    Force WDT reset
Force WDT reset if code jumps to unused program memory
Notes: <number>
<footer>
<header>
<date/time>
Check for (RAM register) = ADDRESS at power up
If any RAM register NOT EQUAL to address then:
  Initialize RAM register = ADDRESS
  Force WDT reset.
Upon power up, this algorithm will init RAM and then force a WDT reset.
The second time through, it will find all of RAM initialized and fall through.

## Slide 218: Robust Design Techniques Robust Software - Subroutine Counting
Maintain subroutine call and execution counters
Increment call counter for every subroutine call
Increment execution counter at the top of every sub-routine
At the top of main loop, check if call and execution counters are equal
If not equal, force a WDT reset
Code Example: ADVRELSW.ASM

## Slide 219: The End Thanks for attending!
Notes: Remind students to take only the PicDem 1, and uniforce demo board. They are to leave the mplab ice, processor module, and picstart + in the class.

## Slide 220: Appendix

## Slide 221: Glossary
TMR0 - 8-bit timer peripheral w/8 bit prescaler
Prescaler - peripheral which delays the TMR0 count by a prescale ratio i.e. 1:1, 1:2, 1:4
Page - memory organization for program memory
Bank - memory organization for data memory
Pipeline - hardware architecture for prefetching an opcode while executing the previous opcode
Orthogonal instruction set - instructions work on ports and registers the same way
OPTION_REG - register of control bits for configuring tmr0, INT, and pull ups
INTCON - register of control bits for configuring peripheral interrupts
STATUS - register of bits indicating the results of an operation
RP1&RP0 - direct addressing bank selection control bits
IRP - indirect addressing bank selection control bit
PORTB - I/O port B
GPIO - I/O port on the 8 pin parts

## Slide 222
The Microchip name, logo, The Embedded Control Solutions Company, PIC, PIC, PICSTART, PICMASTER, PRO MATE, SEEVAL, KEELOQ and the KEELOQ logo are registered trademarks and MPLAB, fuzzyLAB, In-Circuit Serial Programming, ICSP, are trademarks of Microchip Technology Incorporated in the USA and other countries.
Windows is a registered trademark of Microsoft Corporation.
SPI is a trademark of Motorola.
I2C is a registered trademark of Philips Corporation.
Microwire is a registered trademark of National Semiconductor Corporation.
fuzzyTECH is a registered trademark of Inform Software Corporation.
All other trademarks herein are the property of their respective companies.
© 1999 Microchip Technology Incorporated. All rights reserved.
“Information contained in this publication regarding device applications and the like is intended through suggestion only and may be superseded by updates. No representation or warranty is given and no liability is assumed by Microchip Technology Inc. with respect to the accuracy of such information, or infringement of patents arising from any such use of otherwise. Use of Microchip’s products as critical components in life support systems is not authorized except with express written approval by Microchip. No licenses are conveyed, implicitly or otherwise, under any intellectual property rights.”