## Slide 1: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 2: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
let’s initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 3: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 4: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y

## Slide 5: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92

## Slide 6: TCP: retransmission scenarios
X
cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 7: TCP ACK generation [RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap

## Slide 8: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives 3 ACKs for same data
(“triple duplicate ACKs”), resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
(“triple duplicate ACKs”),

## Slide 9: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 10: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 11: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 12: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffering

## Slide 13: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 14: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 15: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 16: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x

## Slide 17: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 18: TCP 3-way handshake: FSM
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket =
newSocket("hostname","port number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for
communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L

## Slide 19: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 20: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB

## Slide 21: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 22: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 23: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 24: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
‘

## Slide 25: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
R/2
R/2
lout
lin
Host B
A

## Slide 26: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
A
Host B

## Slide 27: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
A
Host B

## Slide 28: Causes/costs of congestion: scenario 2
A
lin
lout
l'in
copy
free buffer space!
timeout
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Host B
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 29: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 30: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0

## Slide 31: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin’

## Slide 32: Approaches towards congestion control
two broad approaches towards congestion control:
end-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate for sender to send at

## Slide 33: Case study: ATM ABR congestion control
ABR: available bit rate:
“elastic service”
if sender’s path “underloaded”:
  sender should use available bandwidth
if sender’s path congested:
  sender throttled to minimum guaranteed rate
RM (resource management) cells:
sent by sender, interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
  NI bit: no increase in rate (mild congestion)
  CI bit: congestion indication
RM cells returned to sender by receiver, with bits intact

## Slide 34: Case study: ATM ABR congestion control
two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  senders’ send rate thus max supportable rate on path
EFCI bit in data cells: set to 1 in congested switch
  if data cell preceding RM cell has EFCI set, receiver sets CI bit in returned RM cell
RM cell
data cell

## Slide 35: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 36: TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time

## Slide 37: TCP Congestion Control: details
sender limits transmission:
cwnd is dynamic, function of perceived network congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
LastByteSent-
LastByteAcked
<
cwnd
sender sequence number space
rate
~
~
cwnd
RTT
bytes/sec

## Slide 38: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 39: TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)

## Slide 40: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event

## Slide 41: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!

## Slide 42: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec

## Slide 43: TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L

## Slide 44: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 45: Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 46: Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 47: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”