## Slide 1: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 2: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
examples:
  file distribution (BitTorrent)
  Streaming (KanKan)
  VoIP (Skype)

## Slide 3: File distribution: client-server vs P2P
Question: how much time to distribute file (size F) from one server to N peers?
  peer upload/download capacity is limited resource
us
uN
dN
server
network (with abundant
bandwidth)
file, size F
us: server upload capacity
ui: peer i upload capacity
di: peer i download capacity
u2
d2
u1
d1
di
ui

## Slide 4: File distribution time: client-server
server transmission: must sequentially send (upload) N file copies:
  time to send one copy: F/us
  time to send N copies: NF/us
increases linearly in N
time to distribute F
to N clients using
client-server approach
Dc-s > max{NF/us,,F/dmin}
client: each client must download file copy
  dmin = min client download rate
  min client download time: F/dmin
us
network
di
ui
F

## Slide 5: File distribution time: P2P
server transmission: must upload at least one copy
  time to send one copy: F/us
time to distribute F
to N clients using
P2P approach
us
network
di
ui
F
DP2P > max{F/us,,F/dmin,,NF/(us + Sui)}
client: each client must download file copy
  min client download time: F/dmin
clients: as aggregate must download NF bits
  max upload rate (limting max download rate) is us + Sui
… but so does this, as each peer brings service capacity
increases linearly in N …

## Slide 6
Client-server vs. P2P: example
client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us

## Slide 7: P2P file distribution: BitTorrent
tracker: tracks peers
participating in torrent
torrent: group of peers exchanging chunks of a file
Alice arrives …
file divided into 256Kb chunks
peers in torrent send/receive file chunks
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent

## Slide 8
peer joining torrent:
  has no chunks, but will accumulate them over time from other peers
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
P2P file distribution: BitTorrent
while downloading, peer uploads chunks to other peers
peer may change peers with whom it exchanges chunks
churn: peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain in torrent

## Slide 9: BitTorrent: requesting, sending file chunks
requesting chunks:
at any given time, different peers have different subsets of file chunks
periodically, Alice asks each peer for list of chunks that they have
Alice requests missing chunks from peers, rarest first
sending chunks: tit-for-tat
Alice sends chunks to those four peers currently sending her chunks at highest rate
  other peers are choked by Alice (do not receive chunks from her)
  re-evaluate top 4 every10 secs
every 30 secs: randomly select another peer, starts sending chunks
  “optimistically unchoke” this peer
  newly chosen peer may join top 4

## Slide 10: BitTorrent: tit-for-tat
(1) Alice “optimistically unchokes” Bob
(2) Alice becomes one of Bob’s top-four providers; Bob reciprocates
(3) Bob becomes one of Alice’s top-four providers
higher upload rate: find better trading partners, get file faster !

## Slide 11: BitTorrent Animation
How BitTorrent Works (explained with cardboard cutouts
Notes: http://www.youtube.com/watch?v=w8_JHgVNsA8

## Slide 12: Distributed Hash Table (DHT)
DHT: a distributed P2P database
database has (key, value) pairs; examples:
  key: ss number; value: human name
  key: movie title; value: IP address
Distribute the (key, value) pairs over the (millions of peers)
a peer queries DHT with key
  DHT returns values that match the key
peers can also insert (key, value) pairs
Application 2-12

## Slide 13: Q: how to assign keys to peers?
central issue:
  assigning (key, value) pairs to peers.
basic idea:
  convert each key to an integer
  Assign integer to each peer
  put (key,value) pair in the peer that is closest to the key
Application 2-13

## Slide 14: DHT identifiers
assign integer identifier to each peer in range [0,2n-1] for some n.
  each identifier represented by n bits.
require each key to be an integer in same range
to get integer key, hash original key
  e.g., key = hash(“Led Zeppelin IV”)
  this is why its is referred to as a distributed “hash” table
Application 2-14

## Slide 15: Assign keys to peers
rule: assign key to the peer that has the closest ID.
convention in lecture: closest is the immediate successor of the key.
e.g., n=4; peers: 1,3,4,5,8,10,12,14;
  key = 13, then successor peer = 14
  key = 15, then successor peer = 1
Application 2-15

## Slide 16: Circular DHT (1)
1
3
4
5
8
10
12
15
each peer only aware of immediate successor and predecessor.
“overlay network”
Application 2-16

## Slide 17: Circular DHT (1)
0001
0011
0100
0101
1000
1010
1100
1111
Who’s responsible
for key 1110 ?
I am
O(N) messages
on avgerage to resolve
query, when there
are N peers
1110
1110
1110
1110
1110
1110
Define closest as closest successor
Application 2-17

## Slide 18: Circular DHT with shortcuts
each peer keeps track of IP addresses of predecessor, successor, short cuts.
reduced from 6 to 2 messages.
possible to design shortcuts so O(log N) neighbors, O(log N) messages in query
1
3
4
5
8
10
12
15
Who’s responsible
for key 1110?
Application 2-18

## Slide 19: Peer churn
example: peer 5 abruptly leaves
peer 4 detects peer 5 departure; makes 8 its immediate successor; asks 8 who its immediate successor is; makes 8’s immediate successor its second successor.
what if peer 13 wants to join?
1
3
4
5
8
10
12
15
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor
Application 2-19

## Slide 20: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 21: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 22: Socket programming
  Two socket types for two transport services:
  UDP: unreliable datagram
  TCP: reliable, byte stream-oriented
  Application Example:
Client reads a line of characters (data) from its keyboard and sends the data to the server.
The server receives the data and converts characters to uppercase.
The server sends the modified data to the client.
The client receives the modified data and displays the line on its screen.

## Slide 23: Socket programming with UDP
UDP: no “connection” between client & server
no handshaking before sending data
sender explicitly attaches IP destination address and port # to each packet
rcvr extracts sender IP address and port# from received packet
UDP: transmitted data may be lost or received out-of-order
Application viewpoint:
UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server

## Slide 24: Client/server socket interaction: UDP
close
clientSocket
read datagram from
clientSocket
create socket:
clientSocket =
socket(AF_INET,SOCK_DGRAM)
Create datagram with server IP and
port=x; send datagram via clientSocket
create socket, port= x:
serverSocket =
socket(AF_INET,SOCK_DGRAM)
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number
Application 2-24
server (running on serverIP)
client

## Slide 25
Example app: UDP client
from socket import *
serverName = ‘hostname’
serverPort = 12000
clientSocket = socket(socket.AF_INET,
socket.SOCK_DGRAM)
message = raw_input(’Input lowercase sentence:’)
clientSocket.sendto(message,(serverName, serverPort))
modifiedMessage, serverAddress =
clientSocket.recvfrom(2048)
print modifiedMessage
clientSocket.close()
Python UDPClient
include Python’s socket
library
create UDP socket for server
get user keyboard
input
Attach server name, port to message; send into socket
print out received string and close socket
read reply characters from
socket into string

## Slide 26
Example app: UDP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET, SOCK_DGRAM)
serverSocket.bind(('', serverPort))
print “The server is ready to receive”
while 1:
message, clientAddress = serverSocket.recvfrom(2048)
modifiedMessage = message.upper()
serverSocket.sendto(modifiedMessage, clientAddress)
Python UDPServer
create UDP socket
bind socket to local port number 12000
loop forever
Read from UDP socket into message, getting client’s address (client IP and port)
send upper case string back to this client

## Slide 27: Socket programming with TCP
client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
client contacts server by:
Creating TCP socket, specifying IP address, port number of server process
when client creates socket: client TCP establishes connection to server TCP
when contacted by client, server TCP creates new socket for server process to communicate with that particular client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
byte-stream transfer (“pipe”)
between client and server
application viewpoint:

## Slide 28: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
serverSocket.accept()
create socket,
port=x, for incoming request:
serverSocket = socket()
create socket,
connect to hostid, port=x
clientSocket = socket()
server (running on hostid)
client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket

## Slide 29
Example app: TCP client
from socket import *
serverName = ’servername’
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort))
sentence = raw_input(‘Input lowercase sentence:’)
clientSocket.send(sentence)
modifiedSentence = clientSocket.recv(1024)
print ‘From Server:’, modifiedSentence
clientSocket.close()
Python TCPClient
create TCP socket for server, remote port 12000
No need to attach server name, port

## Slide 30
Example app: TCP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
print ‘The server is ready to receive’
while 1:
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024)
capitalizedSentence = sentence.upper()
connectionSocket.send(capitalizedSentence)
connectionSocket.close()
Python TCPServer
create TCP welcoming
socket
server begins listening for incoming TCP requests
loop forever
server waits on accept()
for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this client (but not welcoming socket)

## Slide 31: Chapter 2: summary
application architectures
  client-server
  P2P
application service requirements:
  reliability, bandwidth, delay
Internet transport service model
  connection-oriented, reliable: TCP
  unreliable, datagrams: UDP
our study of network apps now complete!
specific protocols:
  HTTP
  FTP
  SMTP, POP, IMAP
  DNS
  P2P: BitTorrent, DHT
socket programming: TCP, UDP sockets

## Slide 32
typical request/reply message exchange:
  client requests info or service
  server responds with data, status code
message formats:
  headers: fields giving info about data
  data: info being communicated
important themes:
control vs. data msgs
  in-band, out-of-band
centralized vs. decentralized
stateless vs. stateful
reliable vs. unreliable msg transfer
“complexity at network edge”
Chapter 2: summary
most importantly: learned about protocols!