## Slide 1: CSSE 132 Build ALU with Verilog
Thursday, March 7, 2019

## Slide 2: Questions
How to add more features to the ALU?
  Overflow detector (cont.)
  Zero detector
How to program the gates -- Verilog?
Notes: Do a quick recap on the top-down view.

## Slide 3: ALU (adding Zero Detector)
Why zero detector?
  Set less than  a – b < 0
  Set on equal  a – b = 0
All results return 0

## Slide 4: ALU (adding Overflow Detector)
For addition

## Slide 5: ALU (Overflow Detector cont.)
For addition

## Slide 6: ALU (Overflow Detection cont.)
For Subtraction
  Binv = 1

## Slide 7: Introduce to Verilog
Hardware Description Language
Basically, it describes how to design circuits out of gates.
All things in Verilog happen in parallel.

## Slide 8: Verilog: Basic Syntax
No braces, instead begin and end
Components are enclosed in module tags.
Each module name is followed by a list of inputs and outputs
Notes: Show a demo vlog_and.v

## Slide 9: Verilog: Variables
Types
  wire : Just wires, used for combinational logic.
  reg : similar to registers: used for sequential (and sometimes combinational).
Assignment
  – Blocking assignment (=): execution pauses until this is done.
  – Non-Blocking assignment (<=): happens in parallel to everything else.
Busses: arrays of wires.
  – Declare: wire [15:0] blah;
  – Assign: foo = 16’b0010101111110101;
  – Reference: foo = blah[15:8];

## Slide 10: Verilog: Variables (cont.)
Values and Radix: s’bxx for size s, base b and value xx.

## Slide 11: Verilog: Time
Everything is in parallel unless you specify.
  Blocking assignments are serialized
  non-blocking are parallel (updated after block completes)
  a single module can have multiple things happening at once!
  indicate delay with the # operator. #5; //waits 5ns
Example: assuming all values are initially zero, what are the values of A and B after executing this Verilog code?

## Slide 12: Verilog: Execution Blocks
begin and end.
A block of things can run once, run repeatedly, or get re-run when something changes.
  Once: initial begin
  Repeated: always begin
  Triggered (on either): always @(var)

## Slide 13: Verilog: Abstract concepts
These are extras for the simulator and are useful for writing test fixtures.
  $write : like printf
  $display : like printf with newline
  $finish : halts the simulation

## Slide 14: Verilog: Selection
Similar to C
Notes: Examples in examples/alu4b.v.

## Slide 15: Verilog: Looping
Similar to C