## Slide 1: CSSE 132 Sequential Logic
Thursday, September 19, 2019

## Slide 2: Questions
What is sequential logic?
How to store information in computer with sequential circuit?
  Latches/Flip Flops
Let’s build the most basic memory unit – register.
Notes: Do a quick recap on the top-down view.

## Slide 3: Introducing Sequential logic
Combinational logic: The output only depends on the input
Sequential logic: The output depends on the input plus the current state.

## Slide 4: Problem: How to set value

## Slide 5: Implementation -- SR Latch
R = 0, S = 0:
  Q = 0, Q+ = 0
  Q = 1, Q+ = 1
R = 0, S = 1:
  Q = 0, Q+ = 1
  Q = 1, Q+ = 1
R = 1, S = 0:
  Q = 0, Q+ = 0
  Q = 1, Q+ = 0
R = 1, S = 1:
  Forbidden

## Slide 6: D SR Latch
R and S are complicated. Let’s simplify.
Problem?

## Slide 7: D with Enable Latch
D only matter when enable is 1.

## Slide 8: What time to read the data?
A period of time – wherever enabled is set.
  Unstable
What about let’s use just a moment to load?
  Flip-flop
Not this flip-flop!!!

## Slide 9: Flip-flop
Synchronizing (timing)
  Only loads the value on an edge of the clock.
This is a negative-edge-triggered D flip-flop.

## Slide 10: Flip-flop (cont.)
Click to add text

## Slide 11: Making a register
Just like extending the 1-bit adder to multi-bit adder