## Slide 1: CSSE 132 Data Representation II
Thursday, October 17, 2019

## Slide 2: Questions
How to represent fractional numbers?
What is the precision or range?
What your computer really does?

## Slide 3: Recap: C data type

## Slide 4: Fractional binary numbers
Carnegie Mellon
What is 1011.1012?

## Slide 5: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
Carnegie Mellon
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 6: Convert decimal to binary float
Multiply by 2 by shifting left
Try 0.1: 0.0001100110011…
  0.1 x 2 = 0.2 – 0
  0.2 x 2 = 0.4 – 0
  0.4 x 2 = 0.8 – 0
  0.8 x 2 = 1.6 – 1
  0.6 x 2 = 1.2 – 1
  0.2 x 2 = 0.4 – 0
  0.4 x 2 = 0.8 – 0
  0.8 x 2 = 1.6 – 1
  0.6 x 2 = 1.2 – 1

## Slide 7: Range verse Precision
Range: Max – Min
Precision: Minimal tick

## Slide 8: Intuition
How many bits to represent 126,000,000,000?
What about
  12611?

## Slide 9: IEEE 754
Half-precision 16-bit seeeeeffffffffff
  1 bit sign
  5 bit exponent (unsigned)
  10 bit fraction/significand (unsigned)
Formula: −1sign × 2exp−15 × 1.significand
Simple Examples: 0 01111 0000000000 = −10 × 2 15−15 × 1.00000000002 = 1 1 00111 0000000000 = −11 × 2 7−15 × 1.00000000002 = 1 × 2−8 × 1 = 2−8

## Slide 10: IEEE 754 (cont.)
1 bit sign
8 bit exponent (unsigned)
24 bit fraction/significand (unsigned)
Special cases:
  Zeros: sign = 1 or 0, exp = all 0, significand = all 0
  Infinity: sign = 1 or 0, exp = all 1, significand = all 0
  NaN: sign = 1 or 0, exp = all 1, significand = anything not all 0