## Slide 1: CSSE 132 Introduction to Networking
Thursday, May 2, 2019

## Slide 3: Two computers scenario
Physical media
PHY-layer concern: how to form information from signal
  Modulation:
  Coding: 000 is 0, 111 is 1

## Slide 4: Four computers scenario
Naming/Address: who talks to whom
A Forwarder/Repeater: HUB
Who should talk at when: Medium Access Control (MAC)

## Slide 5: One hundred computer
The repeater can be overwhelmed
Selectively Repeater: SWITCH
  It kind of remembers who normally talks with whom (a table)
Now we have a LAN (Local Area Network)

## Slide 6: Connecting two LANs
Bridge: Connecting two same type of networks (e.g., Ethernet to Ethernet)
Router: Connecting different types of networks (e.g., WiFi to Ethernet)
Concerns:
  Routing: how to deliver message through
  ”best” route.

## Slide 7: Many many LANs

## Slide 8: Layers of Network
Different scopes and roles in the network
  PHY: How to carry info thru signal
  MAC: How to coordinate the access of the channel
  Route: How to delivery message via best route
  Transport: How to delivery infomation with certain rate

## Slide 9: Inside a message - Packet

## Slide 10: IP: Naming/Addressing
IPv4: 32bit
  89702E83 = 137.112.46.131
Rose-Hulman IP: 137.112.0.0/16 = 216
Is 232 sufficient? If not, how?
  NAT (Network Address Translation)
  IPv6: 128 bit  2128

## Slide 11: Better Naming: DNS
DNS: Domain Name System
Problems? DNS hack

## Slide 12: Port
A service identifier