## Slide 1: CSSE 132 Boolean Logic
Wednesday, March 11, 2020
Adapted from CMU 15-213/18-213/15-513

## Slide 2: Outline
Ultimate goal: design a circuit that can compute 1 + 1 = 2.
Today, two building blocks:
  How to compute Boolean operations using common logic gates
  How to do binary addition/subtraction.
    A critical problem: Overflow
Notes: Do a quick recap on the top-down view.

## Slide 3: Boolean Algebra
And (All True)
A&B = 1 when both A=1 and B=1
Or (Any True)
A|B = 1 when either A=1 or B=1
Not (Flip)
~A = 1 when A=0
Exclusive-Or (Xor) (Only One True; When Different)
A^B = 1 when either A=1 or B=1, but not both

## Slide 4: Notation and Symbols
AND: &
OR: |
XOR: ⊕ or ^
NOT: or ~

## Slide 5: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
01101001
& 01010101
01000001
01101001
| 01010101
01111101
~ 01010101
10101010
01000001
01111101
10101010
Notes: All of the Properties of Boolean Algebra Apply

## Slide 6: (Foreshadow) Gates can compute
Gates actually know nothing about computation
But we can use their properties to make computation happen.
Make A + B happen using .

## Slide 7: Addition (Unsigned)
Start with decimal example:
  512 + 333
  532 + 379
Binary (working within certain bit width):
  0110 (6) + 0001 (1)
  0110 (6) + 0110 (6)
  1110 (14) + 0110 (6)
Overflow means the answer is wrong
(according to the given data representation)

## Slide 8: Unsigned Addition Summary
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)
0
2w
2w+1
True Sum
Modular Sum
Overflow

## Slide 9: Addition (signed)
1010 (–6) + 1010 (–6)
  = 4 ?
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)
–2w –1
–2w
0
2w –1–1
2w–1
True Sum
Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
Overflow
Overflow

## Slide 10: Subtracting
: Flip the bits and add one (or simply carry in a 1)
Example:
  1010 (–6) – 0001 (1)
  1010 (–6) – 0011 (3)

## Slide 11: Overflow examples
Which are overflow? (all are signed numbers)
  1101 (–3) + 1011 (–5)
  1111 (–1) + 0011 (3)
  0101 (5) + 0111 (7)
Overflow means the answer is wrong

## Slide 12: Overflow discussion
Need more bits than you have
–2w –1
–2w
0
2w –1–1
2w–1
True Sum
Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
Overflow
Overflow