## Slide 1: CSSE 132 Introduction to Networking
Thursday, May 8, 2025

## Slide 2: Modern networking is a tower of abstractions.
Each layer of abstraction exists to solve particular problems.
Let’s talk through these problems today.

## Slide 3: Problem: how can two computers communicate?
Physical connection between two machines (electrical or optical)
Could also do Wifi

## Slide 4: Problem: how can two computers communicate?
NIC – Network Interface Controller
Electrical connection to your computer
Place to attach some sort of cable

## Slide 5: Problem: how can two computers communicate?
Direct connection. Simple, but limited.

## Slide 6: Problem: how can lots of computers communicate?
Direct connections?

## Slide 7: Problem: how can lots of computers communicate?
Direct connections?
Uh oh.

## Slide 8: Problem: how can lots of computers communicate?
Network hub

## Slide 9: Problem: how can lots of computers communicate?
Network hub
  Like a shared wire
  Signal on one port is echoed out all other points

## Slide 10: Problem: how do we talk to one device, instead of all of them?
MAC address
  Media Access Controller
  6 bytes
  Stamped at the factory
  Should be unique[1]
MAC address: 00:15:5d:e1:0f:40
[1] This is kind of a lie.

## Slide 11: Problem: how do we talk to one device, instead of all of them?
Network switch
  Looks like a hub
  Remembers which MAC is on which wire
  Only send the signal out on one wire
switch table
if7: 00:15:5d:e1:0f:40
if12: 08:2e:4d:03:1d:ac
…

## Slide 12: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device

## Slide 13: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device

## Slide 14: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device

## Slide 15: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device

## Slide 16: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device
MILNET, 1984 (split from ARPANET)

## Slide 17: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device
State of the Internet in 1987

## Slide 18: Problem: the Internet got very big.
A switch can’t reasonably learn every MAC for every device
Modern map of the Internet’s underwater fiber optic cables. [https://www.submarinecablemap.com/]

## Slide 19: Problem: the Internet got very big.
Solution: Wide Area Networks
  Nodes are special networking computers (routers)
  Routers direct packets through the WAN
Solution: Local Area Networks
  Consists mostly of user devices and switches
  Have a designated “gateway” router to communicate outside the LAN.
The Internet

## Slide 20: Problem: the Internet got very big.
Solution: a hierarchical addressing scheme
  Internet Protocol (IP)
  4 bytes
  E.g., all 137.112.___.___ addresses are for Rose-Hulman.
(So many more details: subnets, public / private addresses, network address translation, routing protocols, IPv6 addresses…)

## Slide 21: Checkin: layers of abstraction
What problem does each layer solve?
  PHY: How to use physics to carry signal
  Data Link: How to share a signal-carrying medium
  Network: How to deliver data to the correct recipient via the best route
Layers we haven’t talked about yet:
  Transport: How to ensure that your data reaches its destination
  Session: How to deliver data to the right process on your computer
  Remaining layers: take Networks!

## Slide 22: Problem: How to confirm if your data made it to the destination?
TCP: reliable
  Transmission Control Protocol
  Handshakes
  Checksums
  Acknowledgements
  Think: downloading emails, webpages, files
UDP: unreliable
  User Datagram Protocol
  All about speed
  Ignore mistakes
  Think: real-time games, streaming

## Slide 23: Problem: How do programs share network access within one computer?
Send and receive data in packets
Attach an ID number to each packet
  Called “port”
  We need each program to use a different port
  OS will deliver a packet to the process with the matching port

## Slide 24: Inside a message - Packet

## Slide 25: Port

## Slide 26: Better Naming: DNS
DNS: Domain Name System
  Humans don’t like to type IP addresses
Common choices:
  Google: 8.8.8.8
  Cloudflare: 1.1.1.1
  OpenDNS: 208.67.222.222

## Slide 27: Backup slide: IP: Naming/Addressing
IPv4: 32bit
  89702E83 = 137.112.46.131
Rose-Hulman IP: 137.112.0.0/16 = 216
Is 232 sufficient? If not, how?
  NAT (Network Address Translation)
  IPv6: 128 bit  2128