## Slide 1: CSSE 132 Memory Hierarchy
Monday, December 6, 2021

## Slide 2: Questions
How do different types of memory work?
  Static RAM
  Dynamic RAM
  Solid State Drive
  Disk
How to judiciously leverage memory - caching?
Notes: Do a quick recap on the top-down view.

## Slide 3: Where is memory?

## Slide 4: Memory Hierarchy

## Slide 5: Performance specs
 | Data Rate | Density | Cost
SRAM | insane | 6 transistors/bit | $5,000/GB
DRAM | ~100GB/s | 1 transistor/bit | $5/GB
SSD | 500-2,000MB/s | - | $0.02/GB
Hard Disk | 200MB/s | - | $0.01/GB
Internet | 100MB/s | - | 

## Slide 6: Static RAM
Super fast but expensive.
Implemented with latches and flip-flops.
Always active
Mostly volatile*
Used for:
  Register file
  DRAM cache

## Slide 7: Dynamic RAM (DRAM)
Need to be refreshed (also volatile)
Read/Write:
  Row-Access Strobe (RAS)
  Column-Access Strobe (CAS)

## Slide 8: Solid State Drive (SSD)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after about 100,000 repeated writes.
Flash
translation layer
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
I/O bus

## Slide 9: Garbage collection of SSD

## Slide 10: Hard Disk
Spindle
Arm
Actuator
Platters
Image courtesy of Seagate Technology

## Slide 11: Hard Disk Running

## Slide 12: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.

## Slide 13: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 14: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 15: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 16: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 17: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 18: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 19: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 20: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 21: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 22: Disk Access Time
Average time to access some target sector approximated by:
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7,200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 23: Caching
Use a fast memory to mirror a piece of slow memory.
  Cache access time: 100ns
  Memory access time: 5ms
  Cache miss rate: 1% (say a terrible cache)