## Slide 1: 12 – IP, NAT, ICMP, IPv6

## Slide 2: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-layer frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 3: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.

## Slide 4: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Notes: 4000 bytes  3980 bytes of payload + 20 bytes of IP header
Each smaller datagram must now include 20 bytes of IP header  maximum bytes in data field == 1480 bytes

## Slide 5: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
Notes: IP addressing uses dotted-decimal notation  each byte of the address is written in decimal form

## Slide 6: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
subnet
Notes: Top left: 3 hosts are connected to each other without a router.
They could belong to a Ethernet LAN in which the interfaces are interconnected by an Ethernet hub or switch.
The network interconnecting these 3 hosts with the router is called a SUBNET, IP NETWORK, or simply NETWORT.
The Subnet has an address and the hosts and router interfaces have an address

## Slide 7: Subnets
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet.
Subnet mask: /24
(leftmost 24 bits
determine the subnet)
Notes: The notation /24 is referred to as the subnet mask. It says that the leftmost 24 bits determine the subnet address

## Slide 8: Subnets
How many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 9: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
Notes: An organization is typically assigned a block of contiguous addresses with a common prefix (subnet part). Every device on that organization’s network will receive an address from that range.
An ISP can advertise to the rest of the world that all datagrams whose first 23 bits match 200.23.16.0/23 should be sent to it. Within this prefix, there can be several organizations with their own subnets.
That ability to use a single prefix to advertise multiple networks is called address/route aggregation or route summarization.

## Slide 10: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  UNIX: /etc/hosts
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 11: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain its IP address from network server when it joins network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 12: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 13: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs

## Slide 14: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 15: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:
Notes: What if Fly-By-Night-ISP acquires ISPs-R-Us and wants it to advertise for packets to organization 1?

## Slide 16: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 17: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 18: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers

## Slide 19: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 20: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 21: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 22: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 23: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 24: Traceroute and ICMP
Source sends series of UDP segments to dest
  first has TTL =1
  second has TTL=2, etc.
  unlikely port number
When nth datagram arrives to nth router:
  router discards datagram
  and sends to source an ICMP message (type 11, code 0)
  ICMP message includes name of router & IP address
when ICMP message arrives, source calculates RTT
traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” packet (type 3, code 3)
when source gets this ICMP, stops.
Notes: Source sends datagrams with an unlikely port number.
The destination host will send back an ICMP “port unreachable” packet

## Slide 25: IPv6
Initial motivation: 32-bit address space soon to be completely allocated.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 26: IPv6 Header (Cont)
Priority: identify priority among datagrams in flow
Flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
Next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 27: Other Changes from IPv4
Checksum: removed entirely to reduce processing time at each hop
Options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions
Notes: Error checking is already done at the transport layer and link layer. That redundancy should suffice.

## Slide 28: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers