## Slide 1: 14 – Inter/Intra-AS Routing

## Slide 2: Hierarchical Routing
scale: with > 200 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 3: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router
at “edge” of its own AS
has link to router in another AS

## Slide 4: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-As sets entries for external dests

## Slide 5: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 6: Intra-AS Routing
also known as Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 7: RIP ( Routing Information Protocol)
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:
Notes: Hop  number of subnets traversed from source router to destination subnet, including destination subnet.

## Slide 8: RIP: Example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B
Notes: Notice that this a routing table for a DV algorithm. It includes the next router (or via point) in the direction of the destination subnet.
Assume the D --to– z path cost is based on old information.

## Slide 9: RIP: Example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement
Notes: Here, we are still computing the least-cost path.

## Slide 10: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly (?) propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)
Notes: Looping and poison reverse are described beautifully on page 387, using Figure 4.31.

## Slide 11: RIP Table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
Transport
(UDP)
routed
physical
link
network
(IP)
Transprt
(UDP)
routed
forwarding
table

## Slide 12: OSPF (Open Shortest Path First)
“open”: publicly available
uses Link State algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor router
advertisements disseminated to entire AS (via flooding)
  carried in OSPF messages directly over IP (rather than TCP or UDP)

## Slide 13: OSPF “advanced” features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 14: Hierarchical OSPF
boundary router
backbone router
Area 1
Area 2
Area 3
backbone
area
border
routers
internal
routers

## Slide 15: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements only in area
  each node has detailed area topology; only know direction (shortest path) to nets in other areas.
Area border routers: connect to the backbone and thus other areas.
Backbone routers: route traffic between areas.
Boundary routers: connect to other AS’s.

## Slide 16: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 17: BGP basics
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message
Notes: The prefixes are CIDRized prefixes with each prefix representing a subnet of collection of subnets.

## Slide 18: BGP basics: distributing path information
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP to distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
eBGP session
iBGP session
Notes: BGP is extremely complex. Books are written on it. We are just briefly introducing it.

## Slide 19: Path attributes & BGP routes
When advertising a prefix, advert includes BGP attributes.
  prefix + attributes = “route”
Two important attributes:
  AS-PATH: contains the ASs through which the advert for the prefix passed: AS 67 AS 17
  NEXT-HOP: Indicates the specific internal-AS router to next-hop AS. (There may be multiple links from current AS to next-hop-AS.)
When gateway router receives route advert, uses import policy to accept/decline.

## Slide 20: BGP route selection
Router may learn about more than 1 route to some prefix. Router must select route.
Elimination rules:
  Local preference value attribute: policy decision
  Shortest AS-PATH
  Closest NEXT-HOP router: hot potato routing
  Additional criteria

## Slide 21: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 22: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 23: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 24: Why different Intra- and Inter-AS routing ?
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 25: Network Layer: summary
Next stop:
the Data
link layer!
What we’ve covered:
network layer services
routing principles: link state and distance vector
hierarchical routing
IP
Internet routing protocols RIP, OSPF, BGP
what’s inside a router?
IPv6