## Slide 1: Chapter 6: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers!
# wireless Internet-connected devices soon to exceed # wired Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 2: Elements of a wireless network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 3: Elements of a wireless network
network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
Notes: EMPHASIZE

## Slide 4: Elements of a wireless network
network
infrastructure
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
Notes: There are 2 modes in which wireless host can operate:
Infrastructure mode
Ad hoc mode

## Slide 5: Characteristics of selected wireless link standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
3G cellular
enhanced
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data
Notes: EMPHASIZE

## Slide 6: Elements of a wireless network
network
infrastructure
infrastructure mode
base station connects mobiles to wired network
handoff: mobile changes base station providing connection to wired network

## Slide 7: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves
Notes: These nodes form a mobile ad hoc network (MANET) or a vehicular ad hoc network (VANET).

## Slide 8: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET
Notes: EMPHASIZE
Nadine’s research is in the area of wireless mesh networks.

## Slide 9: Wireless Link Characteristics (1)
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects & ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 10: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest thruput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
Notes: Modulation is the process of conveying a message signal in another signal that can be physically transmitted.
For a given modulation scheme, the higher the SNR, the lower the BER.
For a given SNR, a modulation technique with a higher bit transmission rate will have a higher BER.

## Slide 11: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B
Notes: EMPHASIZE
Hidden terminal problem occurs when there is a physical obstruction in the environment.

## Slide 12: Code Division Multiple Access (CDMA)
used in several wireless broadcast channels (cellular, satellite, etc) standards
unique “code” assigned to each user; i.e., code set partitioning
all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
Notes: Recall that when hosts communicate over a shared medium access, a protocol is needed so that the signals sent by multiple senders do not interfere at the receiver.
Channel partitioning protocols
Random access protocols
Taking turns protocols.
CDMA is a channel partitioning protocol.
Receiver must use the sender’s code to decode the encoded message.

## Slide 13: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet
Notes: EMPHASIZE
SSID => Service set ID

## Slide 14: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 15: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK
Notes: Distributed inter-frame spacing (DIFS)
Short inter-frame spacing (SIFS)

## Slide 16: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!
Notes: How do we deal with the hidden terminal problem?
Here is an idea.

## Slide 17: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 18: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode
Notes: 2 => source
1 => destination (AP if source is wireless host, wireless host if AP is source)
3 => since part of subnet, subnets need to be connected to other subnets. 3 => router interface.

## Slide 19
802.11: advanced capabilities
Rate Adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER
Notes: EMPHASIZE

## Slide 20
802.11: advanced capabilities
Power Management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame

## Slide 21
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
Slave device
Parked device (inactive)
P
802.15: personal area network
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps
Notes: There are various types of networks.
PAN network, evolved from Bluetooth specs.

## Slide 22
802.16: WiMAX
like 802.11 & cellular: base station model
  transmissions to/from base station by hosts with omnidirectional antenna
  base station-to-base station backhaul with point-to-point antenna
unlike 802.11:
  range ~ 6 miles (“city rather than coffee shop”)
  ~14 Mbps
point-to-multipoint
point-to-point
Notes: EMPHASIZE
Yet another type of network
(World interoperability for microwave access) aims to deliver wireless data to a large number of users over a wide area at cable model and ADLS rates.
Aims at supporting mobility at speeds of up to 80 mph.
It resembles both wifi (in infrastructure mode) and cellular networks.

## Slide 23
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wide area net
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 24: Cellular standards: brief survey
2G systems: voice channels
IS-136 TDMA: combined FDMA/TDMA (North America)
GSM (global system for mobile communications): combined FDMA/TDMA
  most widely deployed
IS-95 CDMA: code division multiple access
IS-136
GSM
IS-95
GPRS
EDGE
CDMA-2000
UMTS
TDMA/FDMA
Don’t drown in a bowl
of alphabet soup: use this
for reference only

## Slide 25: Cellular standards: brief survey
2.5 G systems: voice and data channels
for those who could not wait for 3G or 4G service: 2G extensions
general packet radio service (GPRS)
  evolved from GSM
  data sent on multiple channels (if available)
enhanced data rates for global evolution (EDGE)
  also evolved from GSM, using enhanced modulation
  data rates up to 384K
CDMA-2000 (phase 1)
  data rates up to 144K
  evolved from IS-95

## Slide 26: Cellular standards: brief survey
3G systems: voice/data
Universal Mobile Telecommunications Service (UMTS)
  data service: High Speed Uplink/Downlink packet Access (HSDPA/HSUPA): 3 Mbps
CDMA-2000: CDMA in TDMA slots
  data service: 1xEvolution Data Optimized (1xEVDO) up to 14 Mbps
….. more (and more interesting) cellular topics due to mobility (stay tuned for details)

## Slide 27
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G (voice) network architecture
MSC
Public
telephone
network
Gateway
MSC
G

## Slide 28
2.5G (voice+data) network architecture
BSC
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel