## Slide 1: 19 – Multimedia Networking

## Slide 2: Multimedia and Quality of Service: What is it?
multimedia applications: network audio and video
(“continuous media”)
network provides application with level of performance needed for application to function.
QoS

## Slide 3: MM Networking Applications
Fundamental characteristics:
typically delay sensitive
  end-to-end delay
  delay jitter
loss tolerant: infrequent losses cause minor glitches
antithesis of data, which are loss intolerant but delay tolerant.
Classes of MM applications:
1) stored streaming
2) live streaming
3) interactive, real-time
  Jitter is the variability
  of packet delays within
  the same packet stream

## Slide 4: Streaming Stored Multimedia
Stored streaming:
media stored at source
transmitted to client
streaming: client playout begins before all data has arrived
timing constraint for still-to-be transmitted data: in time for playout

## Slide 5: Streaming Stored Multimedia: What is it?
1. video
recorded
2. video
sent
3. video received,
played out at client
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network
delay
time

## Slide 6: Streaming Live Multimedia
Examples:
Internet radio talk show
live sporting event
Streaming (as with streaming stored multimedia)
playback buffer
playback can lag tens of seconds after transmission
still have timing constraint
Interactivity
fast forward impossible
rewind, pause possible!

## Slide 7: Real-Time Interactive Multimedia
end-end delay requirements:
  audio: < 150 msec good, < 400 msec OK
    includes application-level (packetization) and network delays
    higher delays noticeable, impair interactivity
applications: IP telephony, video conference, distributed interactive worlds

## Slide 8: Multimedia Over Today’s Internet
TCP/UDP/IP: “best-effort service”
no guarantees on delay, loss
Today’s Internet multimedia applications
use application-level techniques to mitigate
(as best possible) effects of delay, loss
But you said multimedia apps requires
QoS and level of performance to be
effective!
?
?
?
?
?
?
?
?
?
?
?

## Slide 9: Streaming Stored Multimedia
application-level streaming techniques for making the best out of best effort service:
  client-side buffering
  use of UDP versus TCP
  multiple encodings of multimedia
jitter removal
decompression
error concealment
graphical user interface w/ controls for interactivity
Media Player

## Slide 10: User Control of Streaming Media: RTSP
HTTP
does not target multimedia content
no commands for fast forward, etc.
RTSP: RFC 2326
client-server application layer protocol
user control: rewind, fast forward, pause, resume, repositioning, etc…
What it doesn’t do:
doesn’t define how audio/video is encapsulated for streaming over network
doesn’t restrict how streamed media is transported (UDP or TCP possible)
doesn’t specify how media player buffers audio/video

## Slide 11: RTSP: out of band control
FTP uses an “out-of-band” control channel:
file transferred over one TCP connection.
control info (directory changes, file deletion, rename) sent over separate TCP connection
“out-of-band”, “in-band” channels use different port numbers
RTSP messages also sent out-of-band:
RTSP control messages use different port numbers than media stream: out-of-band.
  port 554
media stream is considered “in-band”.

## Slide 12: RTSP Example
Scenario:
metafile communicated to web browser
browser launches player
player sets up an RTSP control connection, data connection to streaming server

## Slide 13: Metafile Example
<title>Twister</title>
<session>
<group language=en lipsync>
<switch>
<track type=audio
e="PCMU/8000/1"
src = "rtsp://audio.example.com/twister/audio.en/lofi">
<track type=audio
e="DVI4/16000/2" pt="90 DVI4/8000/1"
src="rtsp://audio.example.com/twister/audio.en/hifi">
</switch>
<track type="video/jpeg"
src="rtsp://video.example.com/twister/video">
</group>
</session>

## Slide 14: RTSP Operation

## Slide 15: Content distribution networks (CDNs)
Content replication
challenging to stream large files (e.g., video) from single origin server in real time
solution: replicate content at hundreds of servers throughout Internet
  content downloaded to CDN servers ahead of time
  placing content “close” to user avoids impairments (loss, delay) of sending content over long paths
  CDN server typically in edge/access network
origin server
in North America
CDN distribution node
CDN server
in S. America
CDN server
in Europe
CDN server
in Asia

## Slide 16: Content distribution networks (CDNs)
Content replication
CDN (e.g., Akamai) customer is the content provider (e.g., CNN)
CDN replicates customers’ content in CDN servers.
when provider updates content, CDN updates servers
origin server
in North America
CDN distribution node
CDN server
in S. America
CDN server
in Europe
CDN server
in Asia

## Slide 17: CDN example
origin server (www.foo.com)
distributes HTML
replaces:
http://www.foo.com/sports.ruth.gif
with http://www.cdn.com/www.foo.com/sports/ruth.gif
HTTP request for
www.foo.com/sports/sports.html
DNS query for www.cdn.com
HTTP request for
www.cdn.com/www.foo.com/sports/ruth.gif
1
2
3
origin server
CDN’s authoritative
DNS server
CDN server near client
CDN company (cdn.com)
distributes gif files
uses its authoritative DNS server to route redirect requests
client

## Slide 18: More about CDNs
routing requests
CDN creates a “map”, indicating distances from leaf ISPs and CDN nodes
when query arrives at authoritative DNS server:
  server determines ISP from which query originates
  uses “map” to determine best CDN server
CDN nodes create application-layer overlay network

## Slide 19: Summary: Internet Multimedia: bag of tricks
use UDP to avoid TCP congestion control (delays) for time-sensitive traffic
client-side adaptive playout delay: to compensate for delay
server side matches stream bandwidth to available client-to-server path bandwidth
  chose among pre-encoded stream rates
  dynamic server encoding rate
error recovery (on top of UDP)
  FEC, interleaving, error concealment
  retransmissions, time permitting
CDN: bring content closer to clients