# Niusha Rostamkolai

Box 115

# AC Circuits

ECE 204

HW #24

Problems:

1     _____

2     _____

3     _____

- A single-phase 2400/120 V transformer is rated at 6 kVA, and has an equivalent circuit impedance referred to the secondary side of Ze2 = 0.0125 + j0.25 Ω. This transformer is connected to a source that produces a 110 /0o V at the load with the full load current at 0.9 lagging power factor. Calculate:

  - Full load current phasor at the load side in polar form

  - Load impedance in polar form

  - Full load current phasor at the source side in polar form

  - Transformer equivalent impedance referred to the primary side in rectangular form

  - Source voltage phasor in polar form

- The transformer of Problem 1 now is connected to source voltage of 2500 /0o V. The load impedance is still ZL = 2.2 /25.84o Ω. Calculate:

  - Load impedance referred to the primary side in polar form

  - Source current phasor in polar form

  - Load current phasor in polar form

  - Load voltage phasor in polar form

- A 100 kVA, 2300/230 V single-phase transformer has the following parameters:

R1 =0.3 Ω		R2 = 0.0030 Ω			RC = 4.5 kΩ

X1 = 0.65 Ω		X2 = 0.0065 Ω			Xm = 1.0 k Ω

The transformer delivers 75 kW at 230 V and 0.85 power factor lagging. Determine:

- The input current

- The input Voltage

- The input power and power factor