# Niusha Rostamkolai

Box 115

# AC Circuits

ECE 204

HW #25

Problems:

1     _____

2     _____

- Tests are performed on a single-phase, 20 kVA, 2200/220 V, 60 Hz transformer and

the following results are obtained:

| Parameters | Open Circuit Test - LV Side | Short Circuit Test - HV Side |
| --- | --- | --- |
| Voltage (V) | 220 | 205 |
| Current (A) | 1.52 | 9.1 |
| Power (W) | 161 | 465 |

Compute parameters of the approximate equivalent circuit referred to the high voltage

side.

- A 50 kVA 2400/240 V single-phase transformer was tested and the following data

were obtained:

| Parameters | Open Circuit Test - LV Side | Short Circuit Test - HV Side |
| --- | --- | --- |
| Voltage (V) | 240 | 55 |
| Current (A) | 5.0 | 20.8 |
| Power (W) | 450 | 600 |

Compute parameters of the approximate equivalent circuit referred to the high voltage

side and low voltage side.