ECE 452

PSpice Project 2

Single-Phase Half-Wave & Full-Wave Bridge Rectifiers

Objective

The objective of this project is to become familiar with the performance of single-phase half-wave and full-wave bridge diode rectifiers.

Procedure

Implement circuits of Figures 1 and 2 in PSpice. The sinusoidal source (Vsin) has an rms voltage of 120 V and a frequency of 60 Hz. The load has a resistance of 1  in series with an inductance of 5 mH. Diodes have the following characteristics:

Reverse breakdown Voltage = 1600 V

Reverse breakdown Current = 30 mA

Reverse Saturation Current  = 250 A

Figure 1. Half-Wave Rectifier		          Figure 2. Full-Wave Rectifier

1. Plot the instantaneous input voltage and current on one graph, and output voltage

and current on another graph from 0 to 50 ms for the half-wave rectifier.

a. Calculate Fourier coefficients of the output voltage and current with PSpice.

b. Calculate Fourier coefficients of the input voltage and current with PSpice.

c. Compare the harmonic contents of the output and input voltages and currents by

developing two Excel Bar Charts.

d. Calculate the input power factor by hand.

2. Plot the instantaneous input voltage and current on one graph, and output voltage

and current on another graph from 0 to 50 ms for the full-wave rectifier:

a. Calculate Fourier coefficients of the output voltage and current with PSpice.

b. Calculate Fourier coefficients of the input voltage and current with PSpice.

c. Compare the harmonic contents of the output and input voltages and currents by

developing two Excel Bar Charts.

d. Calculate the input power factor by hand.

Report

Write a memo and discuss and compare the results. Attach the PSpice output files and all of your hand calculations to your memo.